## Slide 1: Driftsondes and Dropsondes for Wind Measurements
Holger Vömel, Terry Hock
NCAR EOL
Working Group Meeting on Space‐based Lidar Winds
28 April 2015

## Slide 2: Global Hawk as Platform

## Slide 3: Global Hawk as Platform

## Slide 4: Drops during HS3, 2011 - 2014

## Slide 5: Driftsonde
Iridium Satellite
Ground station
(web based
remote operation)
Driftsonde Gondola
54 dropsondes
Float altitude
~18 to 30 km
Large zero-pressure or
super-pressure balloon
aloft for days to months
Dropssonde :
Pressure
Temperature
Relative humidity
Wind
Sondes dropped on command or a pre-programmed schedule

## Slide 6: Past campaigns
AMMA (2006)
T-PARC (2008)
Pre-Concordiasi (2010)
Concordiasi(2010)

## Slide 7: Miniature In-situ Sounding Technology (MIST Sonde)
Cone Parachute
400 MHz Transmitter
GPS Receiver
GPS Antenna
Temperature Sensor
Humidity Sensors
400 MHz Antenna
Microcontrollers
Lithium
Battery
Pressure Sensor
Back Side Components

## Slide 8: Miniature In-situ Sounding Technology (MIST Sonde)
Vaisala RS-92 radiosonde sensor module
  Pressure, Temperature, Humidity
  Update rate 0.5 sec
Winds based upon OEM GPS receiver
  0.1 m/s resolution
  0.25 sec (4 Hz) update rate for wind data
  Mass: 182 grams

## Slide 9: System Communications and Data Flow
Driftsonde
Gondola
Internet
RF Link
400 MHz
Telephone
Lines
Iridium Ground System
Arizona U.S.
Web Interface
and Control
Web Interface
and Control
Web Interface
and Control
Toulouse
Seychelles
Boulder
Boulder Telephone
Modems (min qty 4)
Boulder Servers
Back End control &
Data Storage
NCAR
Ground
Control
Boulder, CO
Iridium Satellite
RF Link
1620 MHz
RF link
Dropsonde
PTU & Winds

## Slide 10: Dropsondes on other platforms
C-130 Aircraft
P-3 Aircraft
Driftsonde - Zero Pressure balloon
G-5 Aircraft
Driftsonde –Super Pressure Balloon
& UAS Global Hawk

## Slide 11: Pre-Concordiasi Feb – May 2010
Courtesy of CNES
Launch at Seychelles: 8, 19 and 21 February 2010
3 balloons, 3 months each

## Slide 12: Pre-Concordiasi Feb – May 2010
Dropsondes Western Indian Ocean:
Notes: 41 soundings over 37 days from two different driftsonde balloons in the Western Indian Ocean.
It took both payloads about three weeks to reach the African coast.

## Slide 15: Comparisons of measured and analyzed winds
Podglajen, A., et al., J. Geophys. Res. Atmos., 119, 11,166–11,188
Notes: Work by Aurélien Podglajen et al.

## Slide 16: Comparisons of measured and analyzed winds
Podglajen, A., et al., J. Geophys. Res. Atmos., 119, 11,166–11,188
Large, long-lasting errors in the equatorial dynamics in current NWP products
Mostly due to poorly simulated equatorial waves
Main cause of error is the lack of wind observations

## Slide 17: Strateole-2
Strateole-2 long duration drift sonde campaign focuses on tropics in particular tropical tropopause layer
Validation flights planned 2017/2018
Main campaigns planned for 2018/2019 season and launch site TBD
Two campaigns scheduled about one year apart
Funding not yet secure

## Slide 18: Different regions in the tropics
From Vömel et al., 2002
Tropopause
Level of mean convective outflow
Top of tropopause layer
Notes: Challenge:
Identify and quantify regions, that contribute to dehydration
Quantify the importance of the different dehydration processes:
Convective dehydration
Slow scale dehydration
Wave driven dehydration
Superstaturation in clouds
Increase the reliability in water vapor observations
Increase the number of observations
Validate global scale systems
Provide continuity to these observations

## Slide 19: Different regions in the tropics
From Vömel et al., 2002
Tropopause
Level of mean convective outflow
Top of tropopause layer
Strateole-2 region
Notes: Challenge:
Identify and quantify regions, that contribute to dehydration
Quantify the importance of the different dehydration processes:
Convective dehydration
Slow scale dehydration
Wave driven dehydration
Superstaturation in clouds
Increase the reliability in water vapor observations
Increase the number of observations
Validate global scale systems
Provide continuity to these observations

## Slide 20: Campaign plan
Lower altitude in situ flights: 70 hPa, 18.5 km
4 times: Meteorology, particle, ozone, water vapor (TTL1)
4 times: Meteorology, particle, tracer, water vapor (TTL2)
Higher altitude profiling flights: 50 hPa, 20 km
4 times: Meteorology, Lidar, fiber optic, GPS ROC (Strat-1)
12 times: Meteorology, driftsondes (Strat-2)
Second campaign roughly one year later
Notes: Scientific payload weight up to 24 kg including power.

## Slide 21: Summary
Dropsondes provide in situ profiles of winds and PTU on demand
Airborne platforms: NCAR G-V, C130, NOAA G-IV, Global Hawk
Driftsondes carry up to 54 dropsondes per payload.
Driftsondes highly suitable for tropical region and very remote regions
Driftsondes provide profiles between ~20 km and surface

## Slide 23: In situ Instruments
Meteorology: GPS position and horizontal wind (CNES) Pressure and Temperature (LMD)
Water Vapor: Tunable diode laser hygrometer (GSMA) Frost point hygrometer (LMD)
Ozone: UV Ozone photometer (LMD and LASP)
Particle counters: WPC (U. Wyoming) LOAC (LPC2E)
Carbon dioxide/Methane: Tunable diode laser (GSMA)
Radiative fluxes: Upward infrared and visible fluxes (LATMOS)
Notes: GSMA : (Groupe de Spectrométrie Moléculaire et Atmosphérique, Université de Reims
LPC2E-CNRS: Laboratoire de Physique et Chimie de l'Environnement et de l'Espace Université d’Orléans

## Slide 24: Profiling Instruments
Driftsonde: T, wind, P, humidity from balloon altitude to ground (NCAR)
Fiber Optic: Continuous temperature profile measurements within a few kilometers below the balloon (LASP)
GPS Radio-Occultation: Temperature and humidity profiles from balloon altitude to ground (Scripps)
Lidar: Downward looking backscatter profiles at 532 nm (CNR)
Notes: GSMA : (Groupe de Spectrométrie Moléculaire et Atmosphérique, Université de Reims
LPC2E-CNRS: Laboratoire de Physique et Chimie de l'Environnement et de l'Espace Université d’Orléans

## Slide 25
Dropsondes Western Indian Ocean:

## Slide 26
Dropsondes Western Indian Ocean:

## Slide 27: Pre-Concordiasi Feb – May 2010
NCAR
Driftsonde
Payload

## Slide 29: Driftsonde Gondola
MIST Sonde Capacity: 54 units
Operational Life: ~ 6+ weeks
Mass: ~24kg (with sondes)
Size: 71 cm x 71 cm x 45 cm
Power: Lithium SO2 Batteries
Solar Panel Heaters for batteries and electronics
Automated Radiosonde Sounding System
Iridium Satellite Communications
System Health Engineering Monitoring
  Position & Velocity - GPS Receiver
  Pressure Sensor
  Battery voltages
  Solar Panel voltage
  Component Temperatures

## Slide 30: Sonde Fall Velocity

## Slide 31: Miniature In-situ Sounding Technology (MIST Sonde)
Size: 30.5 cm height x 4.40 cm diameter
Mass: 182 grams
Fall time: ~ 17 minutes from 60 mb
Fall Velocity: ~40 m/s @ 60 mb, ~10 m/s @ surface
Vaisala RS-92 radiosonde sensor module
  Pressure, Temperature, Humidity
  Update rate 0.5 sec
Winds based upon OEM GPS receiver
  0.1 m/s resolution
  0.25 sec (4 Hz) update rate for wind data
Cone parachute
Transmission at 403-406 MHz

## Slide 32: Global Operations
Scientific Flight Operations Center & Flight Control
Toulouse, France
Engineering Monitoring
Boulder, USA
Balloon Launch Location
Victoria, Seychelles
Past Launch and Flight Operations Locations

## Slide 33: Pre-Concordiasi Feb – May 2010
Dropsondes Atlantic crossing:
Notes: 19 soundings across the Atlantic on the driftsonde, which was pulled out of the equatorial belt. The Atlantic crossing took 10 days, which means we have about twice daily soundings across this region.

## Slide 36
Dropsondes Atlantic crossing: