## Slide 1
The Cloud-Aerosol Transport System (CATS)
A New Earth Science Capability for ISS
Matthew McGill, Goddard Space Flight Center, Principal Investigator
John Yorks, Goddard Space Flight Center, Science Lead & Algorithms
Charles Trepte, Langley Research Center, Algorithm Support
Hal Maring, NASA HQ, Program Scientist

## Slide 2
The Cloud-Aerosol Transport System (CATS) is a lidar remote sensing instrument built for use on the International Space Station. CATS is a directed opportunity funded by the ISS Program.
    Payload Developer is NASA-Goddard Space Flight Center
    “customer” is the ISS Program (HEOMD)
    SMD is assisting with funding algorithm/processing development (which is a joint effort with LaRC/CALIPSO team)
  CATS was designed to provide vertical profiles of cloud and aerosol properties at up to 3 wavelengths (355, 532, 1064 nm)
CATS is based on existing instrumentation built and operated on the high-altitude NASA ER-2 aircraft
The CATS project has three simultaneous goals:
  Provide long-term (6 months to 3 years) science from ISS
  Prove that low-cost, streamlined project approach can work
  Provide tech demo on-orbit (target ACE mission)
      high rep rate laser
      photon-counting detection
      UV (355 nm) laser operation in space
      HSRL receiver concept
ISS | Earth Science
CATS Overview

## Slide 3
Use what we already have (i.e., the ISS) to achieve rapid results within an affordable budget – essential in our cost-constrained environment
ISS payloads can easily trade mass for cost – the impact on cost can be huge
Embrace strict build-to-cost/build-to-schedule mentality to minimize development cycle and cost – multiple lower-cost Class D instruments can accomplish more than one giant Class B instrument
Incrementally enhance the ISS Earth observing capability, and grow it to become a vital part of the Earth Science system
Build international partnerships for collaborative climate monitoring and exploration
ISS orbit covers significant portion of the Earth’s surface, land area, and populated areas
ISS | Earth Science
Why the ISS makes sense for Earth Science:
Why ISS and Why CATS?
With that rationale, CATS was funded to be a forcing function for Earth Science from ISS and to be a pathfinder for NASA-developed ISS payloads.
Notes: Always remember what CATS is: a demo, a forcing function, an experiment in management….NOT an operational science mission, nor high-reliability.

## Slide 4
ISS provides a low-cost platform for earth science capabilities
CATS will be installed on the Japanese Experiment Module – Exposed Facility (JEM-EF)
Orbit is a 51o inclination orbit at an altitude of about 405 km
  Provides comprehensive coverage of tropics and mid-latitudes
    Primary aerosol transport paths
  Permits study of diurnal changes in clouds/aerosols
Japanese Experiment Module-Exposed
Facility (JEM-EF) on the
International Space Station (ISS)
ISS | Earth Science
ISS Utilization

## Slide 5
JEM-EF
payloads
Japanese Experiment Module – Exposed Facility (JEM-EF)
ISS | Earth Science
ISS & JEM-EF

## Slide 6
CATS Processing Center
NASA GSFC
ISS
Operational Aerosol Forecast Models
VOLCANIC PLUME TRACKING
AIR QUALITY MONITORING
CLOUD PROPERTIES
WILDFIRE DETECTION
AEROSOL PROPERTIES
Research
Forecasting
ISS | Earth Science
CATS Science Applications
Notes: Although CATS is highly programmatic in nature, we DO have real science goals

## Slide 7
Ice Clouds
Water Clouds
Dust
Smoke
Sea Salt
Vertical profiles of backscatter provide important climate information on Earth’s radiation budget
However, layer type (i.e., composition) cannot be determined using backscatter at a single wavelength
Determining layer type is important because:
  Different layers have different microphysical properties which impact radiative balance in different ways
  Climate models need to know the vertical/horizontal distribution and properties of atmospheric layers
  Current climate models do not accurately predict the vertical structure of cloud and aerosol layers
  Lidar data can be used to initialize models for better vertical structure in model output
We want to take the measured profile data
And turn it into a vertically-resolved “feature mask” that identifies the different types of layers.
ISS | Earth Science
Backscatter Measurements
Notes: Layer Typing is important because:
  Current climate models do not accurately predict the vertical structure of cloud and aerosol layers
  Lidar data can be used to initialize models for better vertical structure in model output

## Slide 8
Depolarization ratio (d) provides information about particle shape
Multiple wavelengths provide information about particle size by ratio of the backscatter (color ratio, c)
Both are needed to accurately determine layer type
Ice Clouds:
> 0.40
c > 0.85
Dust:
0.20 < d < 0.30
Water Clouds:
~ 0.0
c > 0.85
Smoke:
c ~ 0.20
ISS | Earth Science
Multiple Wavelengths and Depolarization

## Slide 9: Science Modes
Backscatter: 532, 1064 nm
No HSRL
Depolarization: 532, 1064 nm
Backscatter: 532, 1064 nm
HSRL: 532 nm
Depolarization: 1064 nm
Backscatter: 355, 532, 1064 nm
No HSRL
Depolarization: 532, 1064 nm
Mode 1: Multi-Beam
Mode 2: HSRL Demo
Mode 3: UV Demo
405 km
14.38 m diameter
-0.5o
+0.5o
7 km
LFOV
RFOV
405 km
14.38 m diameter
FFOV
14.38 m diameter
AFOV
405 km

## Slide 10
Laser 1 Type | Nd: YVO4
Laser 1 Wavelengths | 532, 1064 nm
Laser 1 Rep. Rate | 5000 Hz
Laser 1 Output Energy | ~1 mJ/pulse
Laser 2 Type | Nd: YVO4, seeded
Laser 2 Wavelengths | 355, 532, 1064 nm
Laser 2 Rep. Rate | 4000 Hz
Laser 2 Output Energy | ~2 mJ/pulse
Telescope Diameter | 60 cm
View Angle | 0.5 degrees
Telescope FOV | 110 microradians
CATS employs 2 high repetition rate lasers
  One operates at 532, 1064 nm
  Second is seeded to provide narrow linewidth for HSRL measurements and frequency-tripled for use at 355 nm
CATS has a 60 cm beryllium telescope with narrow field-of-view (FOV)
  4 instantaneous fields of view (IFOV)
Primary Power Supply
Telescope
Payload Interface Unit (PIU)
HSRL Detector Box
Telescope Cover
Other Detector Boxes
Laser 1
ISS | Earth Science
CATS Instrument

## Slide 11
ISS | Earth Science
Building the Transceiver
60 cm beryllium telescope,
110 mrad field of view
Laser 2 bench subassembly side
Laser 1 bench subassembly side

## Slide 12
ISS | Earth Science
Integrated and DONE!
The instrument shipped to SpaceX for integration on Sep 30, 2014
Integration to the SpaceX Dragon Trunk completed Oct 8, 2014
Expected launch date was Dec 16, 2014; actual was Jan 10, 2015

## Slide 13
The Cloud-Aerosol Transport System (CATS) is a lidar remote sensing payload utilizing ISS as an affordable Earth Science observing platform.
CATS is designed to study clouds and aerosol properties in the Earth’s atmosphere to
  Monitor effects of climate change
  Monitor dynamic events
  Demonstrate pathfinder instrument for earth science
  CATS is not an operational science mission -- is an experiment.
  CATS provides in-space demonstration of technologies for future satellite missions (e.g., ACE) while demonstrating build-to-cost project development with streamlined management structure.
ISS | Earth Science
CATS Status
TIMELINE
Jan 10: CATS launched on SpaceX5
Jan 22: installed to JEM-EF
Feb 5: “first light” with laser
Feb 10: first “science quality” data
Feb 10: first underflight with aircraft
Feb 12: first continuous 24-hr operation
Feb 17 & 20: additional aircraft underflights
Feb 12- present: continuing operations, as continuously as possible, within operational constraints
  To-date on-orbit:
  Laser #1: 13 billion laser shots, 730+ hrs operation
  Laser #2: 3 ½ billion laser shots, 250+ hrs operation
(that’s abut 65% availability to-date, which is not bad at all for just getting started and dealing with operational constraints of ISS)

## Slide 14
ISS | Earth Science
First Science Data!
L1a data from Feb 11, 1830-1915 UTC. Top image is 532 nm attenuated total backscatter, bottom image is 1064 nm attenuated total backscatter, and the ISS track corresponding to the data.

## Slide 15
ISS | Earth Science
Airborne Validation
Data from Feb 11. Top image is 532 nm normalized relative backscatter (i.e., not yet calibrated) from CATS, bottom image is same for CPL on the ER-2 – the visual correspondence is spectacular.
cirrus cloud heights agree
mid-cloud heights agree
surface return

## Slide 16
ISS | Earth Science
High Rep Rate Works!
This is raw, 350 m x 60 m profile data (1064 nm) – spectacular detail!
This is raw, 350 m x 60 m profile data (1064 nm) – spectacular detail!
CATS is the first on-orbit demonstration of high repetition-rate, photon-counting lidar. This raw data shows excellent detail and fine structure at raw resolution with a paltry 1-2 mJ pulse energy (at least at night).

## Slide 17
ISS | Earth Science
Spectacular Cirrus!
This is raw, 350 m x 60 m profile data (1064 nm) – spectacular detail!
Exceptional cirrus, April 2, 2015
We just happened to be watching the real-time data feed and saw this wonderful cirrus structure.

## Slide 18
ISS | Earth Science
Spectacular Cirrus!
This is raw, 350 m x 60 m profile data (1064 nm) – spectacular detail!
ISS nadir(-ish) video camera view at 13:30:42 UTC, spans ~700 km distance
Exceptional cirrus, April 2, 2015

## Slide 19
ISS | Earth Science
Spectacular Cirrus!
This is raw, 350 m x 60 m profile data (1064 nm) – spectacular detail!
ISS nadir(-ish) video camera view at 13:30:42 UTC, spans ~700 km distance
Exceptional cirrus, April 2, 2015

## Slide 20
ISS | Earth Science
Excellent On-Orbit Demonstration!
This is 350 m x 60 m profile data (1064 nm) – spectacular detail!
Again, excellent structure and detail in the cirrus cloud. Aerosol below is resolved. This is near-aircraft-quality resolution. Preliminary data indicates excellent detection sensitivity using the photon-counting detection.

## Slide 21
ISS | Earth Science
CATS Level-2 Data
This is raw, 350 m x 60 m profile data (1064 nm) – spectacular detail!
Hot off press.
First attempt at cramming data through Level-2 processing to retrieve vertical feature mask.
For first attempt, not bad at all – now moving towards processing backlog of data and settling in to regular processing routine.

## Slide 22
  CATS is a spectacular opportunity, and the latitude given by the ISS Program to apply sound engineering and management judgment in the pursuit of generating good science has been demonstrated to work.
      ISS Program trusted the Payload Developer to derive our own science requirements instead of subjecting the project to externally-derived requirements and oversight
  Instrument design and requirements are consistent with the [self-generated] science requirements.
CATS team has proven that a large attached payload can be built for ~$15M and ~2 years development time.
    On-time/on-cost completion
    Succesfully launched and operating
  The CATS experience and approach is directly applicable to Earth Venture Instrument (EVi) and Earth Venture Mission (EVm) competitive opportunities.
  The GSFC Class D Constitution has been an important outcome of the CATS effort.
ISS | Earth Science
Summary
http://cats.gsfc.nasa.gov
Notes: From customer’s standpoint, we met our goals before even launched.