## Slide 1: Upendra N. Singh, Mulugeta Petros, Jirong Yu, and Michael J. Kavaya NASA Langley Research Center, Hampton, Virginia 23681 USA Timothy Shuman and Floyd Hovis Fibertek, Inc, Herndon, Virginia, USA (757).864.1570 Upendra.N.Singh@nasa.gov
Development of a Space-qualifiable, Conductively-cooled 2-micron Coherent Lidar Transmitter for Global Wind Measurements
Acknowledgements: The authors appreciate the support of George J. Komar, NASA Earth Science Technology Office and Ramesh K. Kakar Science Mission Directorate at NASA HQ
Working Group on Space-based Lidar Winds
Boulder, Colorado
April 28-29, 2015,

## Slide 2: Outline
  Background and motivation
  Technology Development
  Compact 2µm wind lidar transceiver
  Conductive cooled 2µm Oscillator/Amplifier development
  Ground and Airborne campaigns
  Fully Conductively-cooled Risk Reduction Laser
  Conclusions

## Slide 3
Background and Motivation

## Slide 4: Motivation for 2µm Laser/Lidar Development NRC Recommended “3-D Winds” Mission
Global Winds 9 Societal Benefits | 
Extreme Weather Warnings | P
Human Health | P
Earthquake Early Warning | 
Improved Weather Prediction | P#1
Sea-Level Rise | 
Climate Prediction | 
Freshwater Availability | 
Ecosystem Services | 
Air Quality | P
“Knowledge derived from global tropospheric wind measurement is an important constituent of our overall understanding of climate behavior.” [1]
[1] Baker et al, Lidar measured Wind Profiles – The Missing Link in the Global Observing System, Bulletin American Meteorological Society 95 (4), 515-519 (April 2014)

## Slide 5: Early Mission Concept for Earth Winds Laser Atmospheric Wind Sounder (LAWS)
525 km orbit height
Single, pulsed coherent Doppler lidar system covers troposphere
Line of sight (LOS) wind profiles from each laser shot
CO2 TEA laser at 9 microns with high voltage discharge pumping & catalyst to repair gas
~ 20 J pulse energy at 10 Hz
Continuously rotating 1.5-m diameter telescope/scanner
HgCdTe detector cooled to 77K by mechanical cryo-cooler
Required: eye-safe laser

## Slide 6
Laser Technology Development
for Coherent Doppler Lidar

## Slide 7
Laser Technology Development
for Coherent Doppler Lidar
Adapted as mission design and coherent lidar requirements changed
Conducted in parallel with direct detection Doppler lidar development
Part of NASA’s Laser Risk Reduction Program (FY02 – FY10)
Comprised technology development, ground and airborne technology validation, and scientific use of technology
Series of several individual projects
Validation and scientific use of liquid-cooled laser in parallel with laser advancement to conductive-cooled

## Slide 8: Basic Performance Goals for 2-µm Doppler Lidar
Wavelength | 2.053 -µm
Laser Pulse Energy | 250 mJ
Repetition Rate | 10 Hz
Pulse Width | >150 ns
Beam Quality | M2 < 1.2
Pulse Spectrum | Single frequency (seeded)
Cooling | Conductively cooled via heat pipes
Laser Size | 23.9” x 14” x 7.7” (L x W x H) Including heat pipes and condenser

## Slide 9: Parallel Hybrid Doppler Lidar Development, Validation, Space Qualification
2 -µm laser
Hybrid Demonstration
UAV Operation
Hybrid Aircraft Operation
Compact Packaging
Space Qualif.
Pre-Launch Validation
Doppler Lidar Ground Demo.
Conductive Cooling Techn.
Hybrid Operational
Autonomous Oper. Technol.
Space Qualif.
Pre-Launch Validation
2-µm Coherent Doppler Lidar
0.355-µm Direct Detection Doppler Lidar
Diode Pump Technology
Inj. Seeding Technology
Autonomous Oper. Technol.
1 µm laser
Compact Packaging
Doppler Lidar Ground Demo.
Conductive Cooling Techn.
Diode Pump Technology
Inj. Seeding Technology
High Energy Technology
High Energy Technology
Lifetime Validation
Lifetime Validation
7-Yr. Lifetime Validation
7-Yr. Lifetime Validation
Global Winds Approach Using Hybrid Doppler Lidar

## Slide 10
Pulsed
Laser Development
Atmosphere:
Lower Upper
DIAL: CO2
X3
OPO
DIAL: Ozone
2 Lasers, 4 Techniques, 6 Priority Measurements
0.30-0.32 micron
Backscatter Lidar: Aerosols/Clouds
X2
Surface Mapping, Oceanography
X2
0.355 micron
Altimetry:
1.06 micron
2.05 micron
1 MICRON
Doppler Lidar: Wind
Backscatter Lidar:
Aerosols/Clouds
Direct
0.532 micron
2 MICRON
Key Technologies in Common
Laser Diodes
Laser Induced Damage
Frequency Control
Electrical Efficiency
Heat Removal
Ruggedness
Lifetime
Contamination Tolerance
Laser Risk Reduction Program (LaRC-GSFC)
(NASA HQ Funded Directed Program 2001-2010)
2.05 micron
Doppler Lidar: Coherent Ocean/River
Surface Currents
Coherent
Winds
Noncoherent
Winds
Coherent

## Slide 11: Technology Development, Validation, and Scientific Use
Technology
Science Science
LRRP
DAWN
NRC Decadal Survey
3-D Winds Space Mission
IPP
ATIP
DAWN-AIR1
DAWN-AIR2
GRIP Hurricane Campaign
Venture Class Science Flights
98
01
08
10
08
08
06
09
02
09
08
11
09
10
Ground Intercomparison
12
10
ESTO
ESTO
ESTO
ESTO
SMD-ESD
SMD-ESD
SMD-ESD
SMD-ESD
5 years
SMD-ESD
7 years
SMD-ESD
Technology
DAWN UC-12B
LaRC
13
ACT
12 15
SMD-ESD
Tech
Polar Winds: Greenland Iceland
SMD-ESD
15

## Slide 12: Parallel Advancement of Conductive Cooled with Use of Liquid Cooled

## Slide 13: Laser Technology Maturation
Analysis & Design
Fabrication
System Integration
Testing and Model Verification
Space Qualifiable Design
Quantum Mechanical
Modeling
A fully conductively cooled 2-micron solid-state pulsed laser has been demonstrated for the first time.
Technology Enables: Measurement of global 3-D Winds

## Slide 14: Mobile Ground-Based High Energy Wind Lidar Transceiver – LRRP/DAWN Funded
Table Top Transceiver (Transmitter + Receiver)
90 mJ/pulse, 5 pulses/sec.
3’x4’ Optical Table
(no telescope or scanner)
Engineered Transceiver
250 mJ/pulse, 10 pulses/sec.
5.9” x 11.6” x 26.5”, 75 lbs.;
15 x 29 x 67 cm, 34 kg
(no telescope or scanner)

## Slide 15
Ground and Airborne Campaigns

## Slide 16: Ground-Based Hybrid Wind Lidar Demo
The LaRC mobile lidar is deployed as part of NASA HQ funded Program
Utilized NASA LaRC Compact DAWN Lidar Transceiver for 2-µm lidar
Site at Howard University Research Campus in Beltsville, Maryland
GSFC 355-nm
Doppler lidar
LaRC 2-mm
Doppler lidar

## Slide 17: Comparison of Coherent Lidar and Sonde
Root-mean-square of difference between two sensors for all points shown is 1.06 m/s for wind speed and 5.78 deg. for wind direction

## Slide 18: DC-8 Wind Lidar During GRIP (2010)
Harden the transmitter for airborne application
Add telescope and scanner within the enclosure
Airborne wind measurement during GRIP campaign

## Slide 19
GRIP – 2 Sept 2010 – Hurricane Earl
APR-2 Radar
LASE Aerosols
DAWN SNR
DAWN Wind Speed
DAWN Wind Dir
5 eye “crossings”
~400 minutes data
DC-8 Track

## Slide 20
Ground and Airborne Campaigns
Date | Platform | Location | Objective | Publications
2004-2005 | VALIDAR Trailer | Hampton, VA | Technology Validation | G. J. Koch, J. Y. Beyon, B. W. Barnes, M. Petros, J. Yu, F. Amzajerdian, M. J. Kavaya, and U. N. Singh, “High-Energy 2-micron Doppler Lidar for Wind Measurements,” Opt. Engr. 46(11), 116201-1 to 116201-14 (2007)
Mar 2009 | VALIDAR Trailer | Howard University, Beltsville, MD | Wind Intercomparisons between sensors | Grady J. Koch, Jeffrey Y. Beyon,, Paul J. Petzar, Mulugeta Petros, Jirong Yu, Bo C. Trieu, Michael J. Kavaya, Upendra N. Singh,, Edward A. Modlin, Bruce W. Barnes, and Belay B. Demoz , “Field Testing of a High-Energy 2-Micron Doppler Lidar,” Journal of Applied Remote Sensing, Vol. 4, 043512 (2010) B. Demoz, B. Gentry, T. Bacha, K. Vermeesch, H. Chen, D. Venable, E. Joseph G. Koch, U. Singh, M Boquet, L. Sauvage, “Multi-instrument Wind Comparisons at Howard University Beltsville campus: An update,” Working Group on Space-Based Lidar Winds, Bar Harbor, ME (24-26 Aug 2010)
Sep 2010 | DC-8 | Based Fort Lauderdale, FL | NASA GRIP campaign | M. J. Kavaya, J. Y. Beyon, G. J. Koch, M. Petros, P. J. Petzar, U. N. Singh, B. C. Trieu, and J. Yu, “The Doppler Aerosol Wind Lidar (DAWN) Airborne, Wind-Profiling, Coherent-Detection Lidar System: Overview, Flight Results, and Plans,” Journal of Atmospheric and Oceanic Technology (JTECH) 34 (4), 826-842 (April 2014)
Oct 2011 | VALIDAR Trailer | Fort Story, Virginia Beach, VA | Offshore wind turbine energy research | G. Koch, J. Beyon, E. Modlin, P. Petzar, S. Woll, M. Petros, J. Yu, and M. Kavaya, “Side-scan Doppler lidar for offshore wind energy applications,” J. Appl. Remote Sens. 6(1), 063562 (2012)
Nov 2012 & July 2013 | UC-12B | Ocean off Virginia Beach, VA and Ocean City, MD | Offshore wind turbine energy research & technology validation | Grady J. Koch, Jeffrey Y. Beyon, Larry J. Cowen, Michael J. Kavaya, and Michael S. Grant, “Three-dimensional wind profiling of offshore wind energy areas with airborne Doppler lidar,” Journal of Applied Remote Sensing 8 (1), 083662 (2014)
Oct-Nov 2014 | UC-12B | Kangerlussuaq, Greenland | ADM cal/val investigations & arctic warming science | G. D. Emmitt, M. Kavaya, G. Koch, S. Greco, R. Kakar, and U. Singh, “USA Airborne Participation in ADM Cal/Val and Lessons Learned from Satellite Validation Campaigns,” ADM Cal/Val Workshop, Frascati, Italy (10-13 February 2015)
PLANNED May 2015 | DC-8 | Keflavik, Iceland | ADM cal/val investigations with DLR Dassault Falcon 20E & arctic warming science | 

## Slide 21
Fully Conductively-Cooled Risk Reduction Laser

## Slide 22: LaRC Partnership with Fibertek for Space Qualifiable 2-micron Laser Development for NASA 3-D Wind Mission
Laser Risk Reduction Program (ESTO) - 2001-’10
  LaRC has demonstrated fully conductively cooled oscillator/amplifier to 400 mJ, 5 Hz (08/07)
Partnership with Fibertek:
Innovative Partnership Program (LRRP/ESD/Fibertek)
  3-m cavity, 792 nm pumped, conductively cooled 200 mJ, single frequency output at 5 Hz – first generation
  Advanced Component Technology (LaRC/ESTO/Fibertek)
  Compact, 1.5 meter cavity, 808 nm pumped, fully conductively cooled laser transmitter delivering wind quality 250 mJ 10 Hz output for 3-D Wind mission

## Slide 23: Innovative Partnership Program (LRRP/ESD/Fibertek) 2007-2010 (PI: Singh, Co-I: Yu, Kavaya LaRC; Co-I: Hovis, Fibertek)
Single frequency 2-micron Laser (200 mJ/5Hz) built and delivered by Fibertek to NASA LaRC
2-micron Risk Reduction Laser Transmitter

## Slide 24: Design and Fabrication of a Breadboard, Fully Conductively Cooled, 2-Micron, Pulsed Laser for the 3-D Winds Decadal Survey Mission
PI: Upendra Singh, NASA LaRC
Co-Is/Partners: Jirong Yu, Michael Kavaya, LaRC; Floyd Hovis, Tim Shuman, Fibertek, Inc.
Design and fabricate a space-qualifiable, fully conductively-cooled, 2-micron pulsed laser breadboard meeting the projected 3-D Winds mission requirements
  Utilize improvements in key technologies including high-power, long-life space-proven 804 nm pump diodes; derated diode operation, and heat pipe conductive cooling
Perform a long-duration life test on the laser system to evaluate mission readiness.
  Leverage LaRC 2-micron laser development from earlier efforts
  Utilize Fibertek CALIPSO mission flight laser design and development knowledge
  Upgrade previous Fibertek two-micron laser design for flight-like laser based on space heritage
  Utilize space-ready, sealed cylindrical package
  Perform vacuum test while operating at the output requirements of the 3-D Winds mission
TRLin = 3 TRLout = 5
Complete laser mechanical design update 01/13
and improved laser thermal modeling
Assemble and test heat pipe cooled module 04/13
Fabricate and test ring laser with heat pipe 12/13
cooled module
Install and test amplifiers 03/14
Integrate with canister and test 04/14
Vacuum-test laser 10/14
Complete acceptance testing 07/15
Complete analysis and performance testing 12/15
2-Micron Space Qualifiable Pulsed Laser for 3-D Winds
04/12

## Slide 25: ACT Program Summary
Technical Objective(s)–
  Deliver a ruggedized 2.053 µm MOPA laser with the following parameters:
    250 mJ pulse energy
    10 Hz repetition rate
    Beam quality (M2 ) < 1.2
    >100 ns pulse width
    Conductively cooled via heat pipes
  Reach Technical Readiness Level (TRL) 5 by surviving a thermal-vac test.
Period of Performance – 38 months
Deliverable Items - 2 µm laser meeting the performance requirements after surviving a thermal vac test, monthly technical and financial reports, quarterly and yearly financial reports, thermal vac test definition and results report, oscillator test procedure and results report, final technical report
  2 µm laser transmitter meeting the performance requirements and surviving a thermal-vac test
  Thermal vac test procedure and results report
  Oscillator and amplifier performance report

## Slide 26: Linear Cavity Data
Now reaching energies
expected from a short cavity!

## Slide 27: Current Ring Laser Results – Long Pulse
Expect 80 mJ of Q-switched output for 3.6 J of pump energy
Phase II achieved 3X amplification – on track for 240 mJ
after amplifier pair
10 Hz, 150 A
2.36 mm

## Slide 28: Conductively Cooled Laser Design
Housing itself: 19”L x 11”W x 6.1”H
Complete assembly : 23.9”L x 14”W x 7.7”H
Box dims: 19”x11”x7.1” (LxWxH)
ICESat-2: 16”x11”x4.4” (LxWxH)
Mounting feet for illustration only

## Slide 29: Summary and Conclusions
Past
525 km
12 cross-track positions
1 shot measurement
Continuously rotating 1.5-m telescope
Single coherent Doppler lidar
Gas laser*
20 mJ 2-µm solid state energy*
Space required energy = 20 J*
Energy deficit = 1,000*
2-µm lidar not aircraft validated*
Today
400 km
2 cross-track positions
Multiple shot accumulation
4 stationary 0.5-m telescopes
Dual coherent & direct “hybrid” Doppler lidar
Solid-state eyesafe laser*
1200 mJ 2-µm solid state energy*
Space required energy = 0.25 J*
Energy surplus = 5*
2-µm lidar is aircraft validated*
*coherent

## Slide 30
Questions?