## Slide 1: Lidar Uncertainty Measurement Experiment (LUMEX) (June 24th 2014 – July 13th 2014)
A. Choukulkar1,2, W.A. Brewer2, R.M. Banta2, M. Hardesty1,2, Y. Pichugina1,2, Christoph Senff1,2, S. Sandberg2, A. Weickmann1,2, G. Antoszewski3, B. Carroll3, R. Delgado3, J. K. Lundquist4, M. E. Rhodes4, B. Kosovic5, A. Muschinski6, K. Barr7, D. Wolfe8
1Cooperative Institute for Research in Environmental Sciences, Boulder
2Earth Systems Research Laboratory, National Oceanic and Atmospheric Administration, Boulder
3University of Maryland Baltimore County, Baltimore County
4University of Colorado Boulder
5National Center for Atmospheric Research, Boulder
6North-West Research Associates, Boulder
7Lockheed Martin Coherent Technologies, Boulder
8Physical Sciences Division, National Oceanic and Atmospheric Administration

## Slide 2: Instrumentation and Collaborators
Two WindCube V1s
Profiling lidars
Julie Lundquist et al., University of Colorado Boulder
One WindCube 200S scanning lidar
Ruben Delgado et al., University of Maryland Baltimore County
High Resolution Doppler Lidar (HRDL)
NOAA Atmospheric Remote Sensing Group (ARS)
One ZephIR profiling lidar
Lockheed Martin Coherent Technologies Inc.
BAO Tower sonics instrumented by Andreas Muschinski, North-west Research Associates

## Slide 3: Goals
Sampling error analysis
Ozone flux and turbulence retrieval
Inter-comparison of single Doppler retrieval techniques
Testing dual Doppler retrievals
Study Error of Representativeness
Radar Wind Profiler Development and Evaluation

## Slide 4: Instrument Layout
Inner red circle – 500 m
Outer red circle – 1000 m
BAO Tower
Visitor’s Center
Water Tank Site

## Slide 5: Measurement Uncertainty (for Doppler Lidars)
Total Uncertainty
Sampling Error
Error of Spatial Representativeness
Vector Retrieval Error

## Slide 6: I. Sampling Error Analysis
Notes: Depending on the instrument and measurement strategy, sampling error is introduced in the measurement. For Doppler lidars this is a function of scanning strategy. This part of the experiment will help us to understand the sampling errors in the vertical velocity variance. This product is very useful for air quality applications to understand flux transport and also to determine mixing layer heights. Several analytical techniques (for example: Lenschow et al., 1994 and 2000) to determine sampling error will be tested and validated using this data.

## Slide 7: Why is this important?
Multiple deployment objectives
Windspeed and direction profiles
Aerosol backscatter profiles
Vertical velocity variance profiles
Shallow PPI
High PPI
Shallow RHI
Zenith Stare
0
10
20
minutes
Designing the optimal scan queue

## Slide 8: Case 1: The textbook example
Vertical winds measured on June 29th, 2014

## Slide 9: Case 1: Vertical Velocity Variance Sampling Error (July 29th, 2014 from 19:00 to 21:00 UTC)
Sampling Error calculated using method suggested by Lenschow et al., 1994 and Lenschow et al., 2000

## Slide 10: Case 2: Afternoon period large scale event
Vertical winds measured on June 30th, 2014 from 20:00 to 22:00 UTC

## Slide 11: Case 2: Results from Sampling Error Analysis (July 30th, 2014 from 19:00 to 21:00 UTC)

## Slide 12: II. Study Error of Representativeness
Notes: Depending on the instrument and measurement strategy, sampling error is introduced in the measurement. For Doppler lidars this is a function of scanning strategy. This part of the experiment will help us to understand the sampling errors in the vertical velocity variance. This product is very useful for air quality applications to understand flux transport and also to determine mixing layer heights. Several analytical techniques (for example: Lenschow et al., 1994 and 2000) to determine sampling error will be tested and validated using this data.

## Slide 13: Spatial Footprint of Retrieval Techniques
Doppler Beam Swinging (DBS)
Space resolution = 20 m (vertical)
Time resolution = 2 mins
Velocity Azimuth Display (VAD)
Space resolution = 20 m (vertical)
Time resolution = 10 mins
100 – 150 m
1000 – 5000 m
For HRDL
Modified OI – 2D wind field with Space resolution = 2 x range-gate
Time resolution = Time to complete scan
Notes: An important step when improved forecast models is comparing the forecasts with measurements. However, the question arises whether profiles of wind speed and direction provided by instruments at one location are representative of the wind speed and direction predicted by models for a grid box whose size can vary between 1x1 km2 to 3x3 km2. From this study we hope to have data which will help answer this question. This will enable better interpretation of the model-instrument intercomparison carried out during WFIP-2.

## Slide 14: WindCube V1s Next to Each Other
2 min averaged velocities from 40m to 220m above ground

## Slide 15: WindCube V1s Separated
2 min averaged velocities from 40m to 220m above ground

## Slide 16: WindCube V1s Separated

## Slide 17: Telescoping Observation Network

## Slide 18: Current/Future Work
Extend sampling error analysis using new data gathered during XPIA field study
Determine how spatial representativeness can be accounted for when comparing observations with models
Evaluating various turbulence retrieval strategies

## Slide 19
Thank You

## Slide 21: Calibration
Both WindCube V1s deployed at Water Tank site from June 23rd to June 26th.
WindCube 200S deployed on top of HRDL from June 25th to June 30th.
One WindCube V1 moved to near the BAO tower from June 27th to June 30th.
Objective: To establish the WindCube V1s as standards for comparing dual Doppler retrievals and to understand error of representativeness

## Slide 22: Case 3: Transition period
Vertical winds measured on July 13th, 2014 from 16:00 to 17:00 UTC

## Slide 23: Case 3: Results from Sampling Error Analysis (July 13th, 2014 from 16:00 to 17:00 UTC)