## Slide 1: PolarWinds Campaign I results and plans for Campaign II
G. D. Emmitt, S. Greco and K. Godwin
Simpson Weather Associates
Wind Lidar Working Group Meeting
Boulder, 2015

## Slide 2: NASA’s PolarWinds and ADM Cal/Val
Two Campaigns:
  Campaign 1 November 2014 on UC-12B based Kangerlussuaq, Greenland
  Campaign 2 May 2015 on DC-8 based Keflavik, Iceland
Purposes are to conduct basic polar science investigations and to demonstrate technology readiness for ADM Cal/Val
Critical support from NASA Headquarters (Kakar) and LaRC(Singh)
Science and Instrument Team
  Emmitt (SWA) , Principal Investigator
  M. Kavaya(NASA/LaRC), Technology Lead
  G. Koch (NASA/LaRC), Instrument Chief Engineer
  S. Greco (SWA)
  K.Godwin (SWA)
  D. Bromwich (OSU)
  K. Heins (OSU)
  J. Cassano (CU)
  R. Foster (U Wash)
  M. Shapiro (NCAR)
  D. Winker (NASA/LaRC)

## Slide 3: PolarWinds: Campaigns 1 &2 Science Objectives
Validate numerical model forecasts and reanalysis characterizations of airflow in the lower atmosphere over the open oceans, land, ice sheets and transition zones of the Arctic.
Conduct detailed investigations into the importance of dynamic features such as Arctic low level jets and organized large eddies to the transport and fluxes of heat and energy.
Characterize and study the wind regime of the lower atmosphere over marginal ice zones in the Arctic, where ice drift and other processes are largely controlled by the low-level winds.
Provide real measurements that can be used to validate or compare with existing remote sensing platforms. Three examples will be CALIPSO aerosol measurements , MODIS Atmospheric Motion Vectors and ASCAT Ocean Vector Winds. Additional comparisons will be made with observing systems identified by ESA and the PolarWinds Science Team.

## Slide 4
NASA/LaRC UC-12B
DAWN
2 um
220 mJ
10 Hz
15 cm
Complex terrain
and surfaces
Coastal transitions
Stable Boundary Layer Laboratory
ADM/PolarWinds Campaign1
2014

## Slide 5: Mission Types
Satellite Under Pass (SUP) missions
Model Validation (MVAL) missions
ADM Cal/Val (ADM_CV) missions
OLE experiments
Tip Jet missions
Ice Cap Missions

## Slide 6: Example Campaign 1 Mission Profiles
Satellite Under Pass
ADM LOS Wind Simulations

## Slide 7: Example Campaign 1 Mission Profiles
Greenland Tip Jet Investigation
Model Validation: Land/Sea Boundary

## Slide 8
Cold air flow over ice:
smaller-scale rolls,
near-neutral, possibly
slightly stable
Cold air flow off ice,
over warmer water:
larger-scale rolls, merging,
Broadening, deepening
PBL transition from
roll regime into
convective regime
EDMF Needed

## Slide 9: General Missions Summary
14 flights on 13 days
~ 45.5 science flight hours
22 ADM simulation segments
3 CALIPSO segments
~ 10 MODIS segments
~ 10 ASCAT segments
2 “Tip Jet” missions
Numerous missions overflying the Ice Cap and regions of BL rolls/waves.

## Slide 10
Composite of flight tracks

## Slide 11: ADM/PolarWinds Case Study 11/07/14
Flight Objectives
  Model validation
  ASCAT under flight
  MODIS under flight
  ADM sampling simulation
Coastal
Complex wind patterns predicted by models
DAWN soundings below 3000m

## Slide 12
Area of investigation

## Slide 13
Danish Meteorological Institute 12Z forecast
winds at 5000 (~1500m)

## Slide 14
Area of investigation
Polar WRF surface winds 11/07/14 15Z

## Slide 15
ASCAT ocean vector winds from passes at 13.33 and 15:13 GMT

## Slide 16: Greenland Flight 9 out of 14 11/07/14

## Slide 17
Additional sounding examples for Flight 9
Thin clouds
Weak winds w/
variable directions

## Slide 18: NASA’s PolarWinds and ADM Cal/Val Campaign 2
Based out of Keflavik, Iceland
May 11 – 29, 2015
NASA DC-8 core instrument suite
  DAWN (Nadir port 7)
  Yankee dropsondes (105)
  TWiLiTE (Nadir port 5)
Similar PolarWinds science objectives as in Campaign 1
ADM Cal/Val activities include joint missions with DLR Falcon
  Perform calibration flights with A2D/2um DWLs on Falcon
  Practice under flights for ADM Cal/Val as in Campaign 1

## Slide 19
Ceiling: 12,500m
Cruse: 225 m/s
Minimum: 180 m/s
Range: 8000 km

## Slide 20
NASA Langley DAWN Wind Profiling Lidar on NASA DC-8
Laser, Optics, and Some Electronics in Cargo Level
Centered Nadir Port #7 with Shutter Open
Laser Chillers in Passenger Level
Operator Stations in Passenger Level
2-micron
Pulsed
MOPA
0.25 J
10 Hz
200 ns
15 cm
Step-stare conical scan
30-deg nadir
Dual-balanced heterodyne detection

## Slide 21: TWiLiTE on ER-2

## Slide 23: PolarWinds Campaign 2 Plans
Conduct flights to collect wind profiles suitable for numerical model validation and development. These flight segments will be referred to as MVAL experiments.
Conduct flights to collect wind data along and near the marginal ice zone off the east coast of Greenland. These flight segments will be referred to as SEA_ICE experiments.
Conduct flights to take wind measurements on both sides of the east coast of Greenland to measure katabatic wind flows. In addition, conduct flights to take wind measurements of possible Tip Jets (south of the southern tip) and Barrier winds (off the southeast coast of Greenland). These flight segments will be referred to as WIND experiments.
Another set of potential experiments will be conducted to measure the wake flow around Iceland. These flight segments will be referred to as ICELAND experiments.
Flights will also be conducted to measure the winds over the interior of Greenland with a focus on the Ice Cap and flying directly over the Summit. These flight segments will be referred to as SUMMIT experiments.

## Slide 24: Sea Ice and coastal zones

## Slide 25: Katabatic Flows and LLJ

## Slide 26: Iceland Impacts on Flow

## Slide 27: Ice Cap and Summit

## Slide 28: Supporting Groundbased Observations
Radiosondes launched at 00Z and 12Z at the following sites:
BGAM Ammassalik (65.6,-37.63)
BGEM Aasiaat (68.7, -52.85)
BGBW Narsarsuaq (61.15,-45.43)
Summit (72.57,-38.45)
BGSC Ittoqqortoormiit (70.48, -21.95)
BIKF Keflavik (63.96, -22.6)
BIEG Egilsstadir (65.28, -14.4)
ENJA Jan Mayen (70.93,-8.66)
ENAS Ny-Alesund (78.91, 11.93)
Ground-based commercial DWL´s (Leosphere Windcube 200S) are operated at Keflavik airport and in Reykjavik by the Icelandic Met Office (IMO, contact Sybille von Löwis).
In addition the Icelandic Atmospheric Observatory (IAO, https://www.ncas.ac.uk/index.php/en/about-iao) situated in south-east Iceland near Vik (63°46'29.79"N 17°57'54.32"W) is equipped with a commercial DWL (HALO Photonics) operated by University Leeds (contact Barbara Brooks).
The Greenland Summit Station (72.58°N, 38.48 W, 3216 m ASL) releases 2 radiosondes per day and is equipped with an aerosol lidar from the MPL (micro-pulse lidar) network (contact Ralf Bennartz, Uni Vanderbilt, Wisconsin, Shupe et al. 2013) (http://www.esrl.noaa.gov/gmd/obop/sum/). Online data from an on-going campaign at summit station is available at http://icecaps.ssec.wisc.edu/

## Slide 29: Acknowledgements
This research is being funded by NASA.
Credit goes to the DAWN instrument team at NASA/LaRC and the UC-12B crew that flew in challenging weather conditions during Campaign 1