## Slide 1: SINGLE FREQUENCY LASER DEVELOPMENT FOR MARS WIND LIDAR
Patrick M. Burns, Floyd E. Hovis, Kegan Orlowski, Moran Chen, Slava Litvinovitch
13605 Dulles Technology Dr.
Herndon, VA 20171
(703) 471-7671
www.fibertek.com

## Slide 2: Mars Wind Lidar Systems
What and Why?
Lidar designed to measure atmospheric backscatter, depolarization profiles, and wind profiles from polar orbit.
Addresses Mars global 3-D wind structure and how it changes with local time, location, and season
Wind velocities needed for improvement and validation of Global Circulation Models (GCMs)
Knowledge of winds is critical for Entry, Descent, and Landing (EDL)
Fibertek’s part
Development of single frequency 1064nm source with space heritage
Based on laser for Cloud, Aersol, Transport System (CATS) delivered to international space station
Key laser parameters
  Single frequency linewidths < 30MHz
  Energy >5mJ

## Slide 3: Proof of Concept
Assets retained from previous single frequency laser system
  CATS Lidar
  Single frequency Nd:YVO4 MOPA ramp and fire locking
    Ring oscillator
    2 amplifiers
  Reprate:4kHz
  Power: 25W
  Pulsewidth: 6ns
  Linewidth: ~100MHz
Modifications to reduce linewidth<30MHz
  Change oscillator gain medium from Nd:YVO4 to Nd:YAG
  Over-coupled the output coupler
  Stretch pulse >20ns
Adjust
Parameters

## Slide 4: Delivered Test Bed
Allowed development for proof of concept testing of MARLI laser.

## Slide 5: Development of Flight Concept
MARLI system based off CATS design
Lower power, smaller package
57% of CATS footprint and 44% of CATS volume
Desired performance
  Wavelength: 1064nm
  Rep-rate: ≤1kHz
  Energy: 5mJ
  Linewidth: <30MHz
  Beam quality: M2 <2
  Weight of LOM: ~10 kg

## Slide 6: Canister design
Features
Heritage space design concept
  ICESAT-2
  CATS
Canister with rigid midplane
Compartmentalized
  Optical compartment
  Electrical compartment
Flexure mounting system
Pocketing to reduce weight

## Slide 7: STOP (Structural Thermal Optical Performance) analysis
STOP analysis key results:
  beam pointing, beam displacement under environmental simulations (thermal, pressure, vibration, etc.) are manageable
  Able to meet system requirement under predictable environmental loads

## Slide 8: Brassboard Flight Emulator
Brassboard
  Same optical layout as flight design
  Uses same flight heritage mounts
  Thermal interface mimics housing wall
  Allows testing of key parameters and
  performance over temperature

## Slide 9: Laser Architecture & Driving Requirements
Laser Design Features:
MOPA architecture
Ring resonator
Gain heads with resonant end pumping
Polarization output coupling
Injection seeded & ramp and fire locked cavity

## Slide 10: Ramp and fire Locking Scheme
Fibertek uses established ramp and fire injection locking techniques
Ramp and Fire Locking Schematic
Typical ramp and fire dither and resonant signal

## Slide 11: Laser Energy & Pulse Width Results
Laser Energy output=4.6mJ
Standard Deviation of 0.3%
Pulse energy stability reflects stable injection seeding and laser performance
Results in spectral width well below the performance requirements of <30MHz
Good laser energy stability
Temporal pulse width allows
transform limited spectral width<10MHz
Short term Shot-to-shot energy stability:
<1% variation in
shot-to-shot pulse energy

## Slide 12: Beam Quality
Beam Quality M2=1.1
Oscillator Beam quality
Beam Quality M2=1.6
Amplifier Beam quality
Some degradation in beam quality from oscillator to amplifier, but well within performance requirements of M2<2

## Slide 13: Injection Seeding Performance Single Longitudinal Mode Lasing Verified
Unseeded
Seeded & Locked
Scanning Fabry Perot Interferometer
Linewidth~12MHz
Demonstrates a well seeded
cavity

## Slide 14: Summary
Fibertek, Inc. successfully developed and tested Nd:YAG laser system that achieved:
  > 4.5 mJ of 1064 nm from Nd:YAG MOPA Laser
  Ramp and Fire locked
  Injection Seeded and tunable
  Linewidth<30MHz
  Ongoing work: Testing system, paving the way for space flight mission
  Brassboard delivery planned for Q3 2019