## Slide 1: New AMV Wind and Height Measurements from Stereoscopic Views with MODIS-GOES and MISR-GOES Imagery
Dong L Wu1, James L Carr2, and Michael A Kelly3
NASA Goddard Space Flight Center
Carr Astronautics
Applied Physics Lab, Johns Hopkins University
Working Group Meeting for Space Lidar Winds, Hampton, VA July 10-11, 2019

## Slide 2: Motivations
Global 3D wind observations at mesoscale
  Vertical wind profiles from lidar
  Horizontal wind fields from atmospheric motion vectors (AMVs)
AMV height assignment
  Limitations with IR method
  Limitations with single-platform stereo (e.g. MISR)
  Stereo height from multi-angle, multi-platforms (this work)
Cost-effective solutions for spatiotemporal coverage
  LEO-GEO (this work)
  GEO-GEO (NOAA development)
  Future: LEO-LEO, LEO-GEO

## Slide 3: Atmospheric Motion Vector (AMV)
(Image Credit: CMISS, Univ of Wisc)
Panama
Washington DC
Florida
1000 km
Key observable to NWP
Significant impacts (UK Met study):
  Tropics
  Small scales (<200km)
Limitations
  Height error
  Convection
  Gravity waves

## Slide 4: Ongoing Research with AMVs
IR height assignment error
  Multi cloud layers
  Cloud inhomogeneity
  Inversion layer
  Wind shears
Stereo height
  MISR
  MISR-GOES
  MODIS-GOES
Speed bias
  Effects of convection and waves
Measurement quality control
Observation – Background
Pressure (hPa)
(m/s)
Courtesy of International Wind Working Group (IWWG)
http://cimss.ssec.wisc.edu/iwwg/iwwg.html
Obs faster
Obs slower
Notes: The main aim of the NWP SAF AMV (atmospheric motion vector) monitoring site is to improve our understanding of AMV error characteristics in order to enable improvements to the AMV derivation and their treatment in NWP models.
This is achieved by:
Providing a 3-year rolling archive of O-B monthly monitoring plots displaying differences between AMVs (O) and NWP model background winds (B) valid at the same location and time (see Monthly Monitoring tab). Plots are provided for the Met Office and ECMWF in the same format to enable easy comparisons. Both the AMVs and the model forecast contribute to the differences observed in the plots. Differences between centres suggest model-dependent problems whereas similarities suggest either problems with the AMVs or problems shared by the NWP models.
Producing analysis reports every 2 years to coincide with the International Winds Workshops (see Analysis Reports tab). These are detailed studies reviewing (i) the quality of new datasets and (ii) features observed in the O-B monitoring. Details are included of possible causes of the O-B features and, where relevant, actions that may help to alleviate the problems.
Carrying out some bespoke investigations e.g. to investigate diurnal error characteristics (see Investigations tab).
There are two additional aims of the site:
To provide background information on how AMVs are used in NWP (see NWP tab). As part of this the site hosts information on how AMVs are assimilated at different NWP centres.
To provide links for those interested in near real-time monitoring issues (see Real-time Monitoring tab).

## Slide 5
Stereo Height:
Multi-angles from a single platform (e.g. MISR)
~7 min
Aliasing problem
between height and along-track wind

## Slide 6
(JAMC 2017)
MISR-GOES
MISR-MODIS

## Slide 7
Effects of Stereo Height:
Single-angle from multi platforms (e.g. Dual-MetOp)
Height assignment error => Wind error
Cotton et al. (UK Met, 2016)
MetOp-A
MetOp-B
45 min Later

## Slide 8
Solution #1:
GOES - GOES (stereo height and winds)
Hasler (1981)
Black (1982)
Fujita and Dodge (1982)
Shenk (1971) Apollo6
60°

## Slide 9
Hasler et al. (1991)

## Slide 10
Mack et al. (1983)

## Slide 11
NOAA/STAR Program
Jaime Daniels
Wayne Bresky
Results
3D-Winds code prototyped
Compared to operational Visible, IR, and WV winds
Validated with MISR-GOES code and terrain retrievals with good results
Advanced GOES 16/17 Systems:
Accurate Image Navigation and Registration (INR) for Stereo Matching
B02
Visible
Height
New NOAA/STAR Study
Develop 3D-Winds capability for G-16 and G-17
Validate 3D-Wind retrievals
James L. Carr1*, Houria Madani1 (2019)

## Slide 12
Solution #2:
MISR (stereo height) + GOES (winds)
Enabled by advanced GOES-R spatial resolution and INR
Accuracy from 2.2 km sampling:
Height 200 m
Wind <0.5 m/s
New algorithm mitigates GEO height assignment (GOES) and LEO aliasing (MISR) issues

## Slide 13
Validation over Clear-Sky Terrain
Estimated Height Uncertainty: <200m
Estimated Wind Uncertainty <0.5m/s

## Slide 14
Florence (2018)
Low-altitude winds
feeding in warm, moist air
One Frame of
30-Second
GOES MESO
Imagery
PBL
GOES MESO Imagery
Height
15.8 km
0.6 km

## Slide 15
Solution #3: MODIS + GOES
Larger swath coverage
Two angular looks from two platforms (i.e., LEO and GEO)
No synchronization required for LEO and GEO images
Winds from GEO rapid refresh
(Carr et al., 2019; paper in preparation)

## Slide 16
Severe Weather
From Cold Arctic Air
Jan 31, 2019
PBL?

## Slide 17
Aqua MODIS
01/24/2011 UTC17:05
Planetary Boundary Layer (PBL) Dynamics in Cold Air Outbreak
PBL structural evolution
Strong surface-PBL coupling (e.g., radiation and latent heat)
Complex cloud microphysics
New York

## Slide 18
Michigan
Lake Superior
Cold Air Outbreak
PBL Processes
Surface heat and moisture fluxes
Cloud and precipitation interactions
Severe downstream precipitation
(lake effect)
Jan 31, 2019
Clouds or Not?
Cloud detection:
Wind speed < 0.5 m/s; and
Height > 300 m (lidar-like)

## Slide 19
Michigan
Lake Superior
Cold Air Outbreak
(Rapid PBL wind changes on Feb 1, 2019)
Courtesy of
Diego Principe and Houria Madani
PBL Processes
Surface heat and moisture fluxes
Cloud and precipitation interactions
Severe downstream precipitation
(lake effect)

## Slide 20
Hurricane Michael (Oct 9, 2018)
Intensification from Cat 3 to Cat 5 in two days
74 deaths with damage of $25B
MODIS-GOES 3D Winds
Rapid Intensification
CONUS + MESO Sampling

## Slide 21
GOES
MODIS
Singularity
Caveats
No clear-sky winds (where DWL can); Terrain for validating height and geo-registration of imagers
Wind and height uncertainties sensitive to geo-registration error (both MODIS and GOES-16/17 have 0.1-0.2 pixel pointing accuracy)
Singularity spot for LEOs with single look
Accuracy away from singularity (under evaluation):
Height ~300 m
Wind <0.5 m/s
MODIS-GOES:
Pathfinder for Other Operational LEOs and GEOs

## Slide 22
Solution #4: LEO-GEO and DWL
Constellation (GPM-like)
CubeSat
CubeSat
CubeSat
DWL
Instrument: Compact Midwave IR System (CMIS) – ESTO IIP’16

## Slide 23
30°
30°
5-10 min
30°
30°
CubeSat
CubeSat
LEO-LEO (Leader-Follower)
Constellation

## Slide 24: Summary
Global 3D winds at mesoscale
AMV height assignment
Affordable spatiotemporal coverage from stereo AMVs
Synergy of lidar winds and AMVs (curtain clear-sky + areal cloudy coverage)
Stereo height from images on dual platforms without sensor synchronization
LEO CubeSat constellation (polar, global)
LEO-GEO (regional)
GEO-GEO (regional)