## Slide 1: A Roadmap For Meeting Full Tropospheric Wind Measurement Needs
Sara C. Tucker & Carl Weimer
Ball Aerospace and Technologies Corp
Mike Hardesty
University of Colorado, CIRES and NOAA/ESRL

## Slide 2: Motivation
2017 Earth Science Decadal Survey
  Wind lidar in incubation and Explorer categories
NOAA Satellite Observing System Architecture (NSOSA) Study and the Space-Platform Requirements Working Group (SPRWG)
  Full-tropospheric winds (likely from Wind Lidar) wanted by 2030
  How do we get there from here?
  1. First, where are we? Farther along than last DS.
  2. What are the goals & requirements (for NASA and for NOAA)
  3. What paths can we take to get there?
Some perspectives (only 11 years in) and roadmaps

## Slide 3: Wind Lidar Missions: Past
Optical (feature tracking lidar)
Optical Doppler Lidar
A
M
Molecular: UT/LS
Aerosol: LT/clouds
Measure 3D Winds
Active
Passive
Microwave
PBL/aerosol scattering
A
Full-Troposphere & Lower Stratosphere
M
A
“Coherent” Heterodyne Detection
A
LaRC
DAWN
~2 μm, (1.6 μm, ~10 μm)
NOAA CSD, Halo, Leosphere,
“Direct” Detection
Double-Edge
Fringe Imaging
Mach Zehnder
A
M
A
M
A
M
ESA’s Aeolus
GSFC?
UPMC (France)
ATHENA OAWL
1064 nm, 532 nm (CALIPSO) & 355 nm
Nested OAWL
Mission definition
Mission Architecture

## Slide 4: Atmospheric Backscatter
Longer wavelengths
  Larger aerosols present in the PBL & aerosol/cloud layers
  Less atmos. extinction, but less coverage
Shorter wavelengths
  More scattering from PBL and cloud layers
  Scattering off of smaller particles in UTLS
  Molecular scattering
These properties factor strongly into which lidars are best for a given application
Log scale

## Slide 5
Direct Detection
CO2
Solid State Heterodyne
GTWS
GWOS
WISSCR
ATHENA-OAWL
Edge Technique
Fringe Imaging HRDI
Zephyr
GLOW Double Edge
Fringe Imaging Lidar
GroundWinds
A2D Airborne
Optical Autocovariance
TWiLiTE IIP
TWiLiTE AITT
 TWiLiTE Flights 
DAWN 1 IIP
DAWN 2 IIP
CCOPE/ADLS (Airborne)
NOAA TeaCO
NOAA Mini-MOPA
LAWS Panel
LAWS Team
SPARCLE
NOAA HRDL
VALIDAR
 DAWN Flights 
NASA/Ball CALIPSO >11 Years on orbit!
launched
Optical Autocovariance (OA) Wind Lidar
Original OA system development at Ball
OAWL Prototype
OAWL IDL
OAWL IIP
AOVT
OAWL OSSE
HAWC-OAWL IIP
HOAWL & FIDDL ACT
ESA’s ADM Aeolus (single look – 355 nm Aerosol & Molecular)
Decadal Survey 3D-Winds Hybrid
Aeolus Launch
History: A partial timeline of space-based Doppler wind lidar
Notes: >30 years of NASA investments in wind lidar technology
  Multiple technology investments from NASA ESTO.
NASA/NOAA Working Group on Space-Based Wind Lidar (“LWG”, formerly the LAWS science team, 1989)
2007 NRC Decadal Survey “3D-Winds” mission (Tier 3): defined as a hybrid of two separate lidar systems, with two different lasers, on one spacecraft.
The past decade:
  Risk tolerance at NASA has decreased significantly
  Budgets have decreased as well: NASA asked to do more and more
  Industry technology investments help to make missions possible
  Contractor efforts are increasingly scrutinized/audited (DCAA)

## Slide 6: Wind Missions Now: Range of objectives?
Per NSOSA: a DWL as part of a larger weather architecture
  DWL for accurate and precise measurements with high vertical resolution
  Good horizontal coverage also desired
  Optimize impact vs. cost curve
Per SPRWG: Require full tropospheric coverage
  Full troposphere: PBL and UTLS required to have desired impact
  Trades on “stripes” and coverage vs. cost
  …
Decadal Survey
  atmospheric winds a “most important” measurement.
  Might have been designated, if not for perceived readiness.
  PBL emphasis – UTLS winds and chemistry missing
  Tropical cyclones?
  Winds as secondary observation for many other science questions
Weather Focus Area
  Atmospheric dynamics, convective processes, etc.
  New approaches to modeling,
  Work that enables improved NWP.
ESTO: science drives the technology development
NOAA Requirements focus on improving NWP: Lives and Property
NASA Requirements: Science. Processes, Modeling, Pre-operational(?)

## Slide 7: Wind Missions Now
Optical feature tracking lidar
Optical Doppler Wind Lidar
A
M
Molecular: UT/LS
Aerosol: LT/clouds
Measure 3D Winds
Active
Passive
Microwave
PBL/aerosol layers
A
Full-Troposphere & Lower Stratosphere
M
A
Horizontal Resolution/Spacing
Vertical Resolution/Spacing
Wind precision
Height assignment precision
Vertical Resolution/Spacing
IR-Sounders
Stereo Imaging
(GOES-16&S Vis, MWIR,…)
Mission definition
Mission Architecture
Yes, and…
Microwave
Sounders
W
Water Vapor Features
W
W
M
A
W
A

## Slide 8: Wind lidar measurements from space: Aerosol & molecular coverage
OAWL: path to full atmospheric wind profiles:
Two wavelengths (same laser) used to measure winds from both aerosols AND molecules
  @ 532 nm – provides precision using aerosol returns
  @ 355 nm – provides coverage using molecular returns
High altitudes: fewer aerosols & clouds, so UV wavelengths are used to measure winds using lidar returns from just molecules (e.g. ESA’s Aeolus mission, UV OAWL)
Airborne & ground DWLs are best for boundary layer studies at scales that would be smeared by space-based orbit speeds (~7.2 km/s)
Aerosol-DWL’s (Green-OAWL, Coherent detection) provide good returns in lower troposphere and where aerosol layers or thin clouds are present

## Slide 9
IR Sounding AMVs where Water Vapor features available: GOES (GEO) and 4-12 LEO Sounders
DWL where air is clear (UTLS): anchors cloud heights to improve AMV results…AND provide true winds along lidar curtain path
Height error bars
Winds error bars
See Folger & Weissman, 2014 & 2016

## Slide 10: Lidar winds: Studies on the swath of AMV improvement when anchored?
Credit: CIMSS , U.Wisconsin-Madison
Credit: NASA

## Slide 11: NSOSA (AMS): Potential timeline for wind lidar technology maturation roadmap: laser focused
2017-2019: ongoing NASA-funded laser transmitter technology development
2020-2022: A 3-year build and test of laser transmitter ETU, managed by NASA with Industry involvement, deliverable to the operational wind lidar system project in early 2023
2019-2020: NOAA funded pre-Phase A lidar system study tasks
2021: Phase A of operational wind lidar system begins
Environmentally tested laser transmitter subsystem delivery in early 2023.
2012
2030
Pre-Phase A
2019-2020
Phase A
2021
Qual. 2023
2013
2016
Aeolus

## Slide 12: Getting to operational: Full Troposphere
Not just about lasers….systems
2012
now
2030
Pre-Phase A
2019-2020
Phase A
2021
Qual. 2023
2013
2016
OAWL Prototype Demo
GrOAWL 2-look airborne demo
EVI-2 on ISS
Cat. 3
EVI-4 on ISS
Cat. 2
Current TRL Qualifications
HEUVD
HAWC-OAWL (2, 2 look)
ESDS Incubation
Full Trop winds system Demo
TMCO Approval
CALIPSO
ESDS
NSOSA
Aeolus
Flight qual. EDUs
ESDS Explorer
2030 NOAA 3D-Winds
Hardware/Mission
Forcing functions
Sounder demos
Short OPD MZI* OAWL
OSSEs
*nested or not

## Slide 13: Science and Operational Winds
now
2030
Pre-Phase A
2019-2020
Phase A
2021
Qual. 2023
HEUVD
ESDS Incubation
Full Trop winds system Demo
Aeolus
Flight qual. EDUs
ESDS Explorer
2030 NOAA 3D-Winds
Sounder demos
OSSEs & more
Coherent Airborne PBL science
Coherent System Laser Space Qualification
Coherent System Space Qualification
Aerosol/Cloud mission definition
Airborne PBL science missions
Cal/Val
Airborne OAWL Flight demos
Cal/Val
Test Flights
Test Flights
EVI-5,6?

## Slide 14: Roadmaps: More than just Systems and TRL
Technology Development
  Technical Readiness
  Full enterprise participation
  NASA Systems Engineering Handbook definitions 
Mission Development
  Coverage: # spacecraft
  Orbit, Spacecraft, Launch
  Ground System (low latency!)
Mission Science Development
  Science Readiness
  Data products, ATDB
  Data assimilation
  Calibration/Validation
Learn from Aeolus & CALIPSO

## Slide 15
Receiver
Laser
Elect. & SW
Data & Science
Mission
TRL
Concept
Lab demos
Aircraft Demos
Ground demos
Performance scaling to space
2λ Winds
HSRL, GOLD,
& TWiLiTE
OAWL1& GrOAWL lasers
HEUVD
Lifetime-testing
National Instruments/ Labview
PC EDU w/ space-qualified equivalents
Instrument Design Lab
EVI-2 (2013)
proposal
EVI-4 (2016)
proposal
ATBD
Cal-Val planning
Science Implementation Plan
OSSEs
Real-time processed winds (FPGA)
Brassboard IFO EDU build & test
System Thermal/Vacuum/ Shock/Vibe Testing
1 2 3 4 5 6 7 8 9
355 OSSE
NASA/Ball CALIPSO >11 Years on orbit!
PC w/ Space-qualified parts
CALIPSO & ICESAT
telescopes, detectors
Thermal/vacuum/ shock/vibe test
Thermal/vacuum/ shock/vibe test
Payload Controller (PC) & data acq. development
Environmental Test
ESA’s Aeolus (355 nm lasers)
Free-flyer mission designs
2λ OSSE
Airborne flight tests
2λ synergy studies
Ground Validation
Airborne Validation

## Slide 16: Extras

## Slide 17: Passive, Yes, AND aerosol + molecular wind lidar
Aircraft (in-situ)
Visible or water vapor channels
Requires 3 cloud images, cloud brightness temp, cloud mask, cloud height, cloud top pressure
Requires Cloud/WV Features
Motion Vector (aerosol/cloud tracking)
In-situ Profiling
Aircraft
Radiosondes
Surface Buoys
Surface
Scatterometry
Extend winds vertically
Improve precision and vertical resolution
Provide profiles over oceans and SH

## Slide 18: Atmospheric Motion Vectors and lidar
Cloud Drift and WV
GEO:
  GOES/Himawari8/MeteoSat/etc., Visible and IR
Polar:
  MODIS Cloud Drift Winds (Arctic, Antarctic, Aqua, Terra), AVHRR (Arctic, MetOp-B), VIIRS (Arctic)
Height Assignment Uncertainty
  Up to 70% of AMV error (Velden & Bedka, 2009)
Using CALIPSO to assign heights
  Folger & Weissman, (2014 & 2016): used CALIPSO cloud height measurements to anchor Meteosat-10 AMV layer heights
  Up to 15% improvement in co-located (50km, 30 min.) AMVs vectors from Metosat-10.
  lidar-based height bias adjustments (from previous days) resulted in up to 7% improvement, affecting all AMVs
Will multiple sounders drive down the height assignment errors?

## Slide 19: OAWL: Looking Ahead
ESDS Wind Lidar Explorer Mission
ATHENA-OAWL EV-I Concept
Airborne Science
Missions (Cal-Val, EV-S, etc.)
HAWC-OAWL IIP
2, 2 look
EVI-Science Demo on ISS
ATHENA-OAWL Venture-Tech (airborne)
HEUVD (Fibertek)
2030
Operational Winds Missions (NOAA, DoD, NASA, commercial)
NASA ESTO & ESSP Tech Development
Ball Technology Development & Intellectual Property
Science Community Input
Future Science/Mission Opportunities
Interferometer & Full trop IRADs
Aeolus Experience
Earth Science Decadal Survey
NSOSA Needs
Full Trop winds system Demo
Flight qualified EDU
ESDS Incubation
Aerosol Winds
or
Full Tropo-sphere?
TMCO approved
Sounder Demos
Notes: Ball has made investments to invent and develop the technologies
ESTO investments enable Ball to incorporate our technologies into engineering demonstration systems and science studies
Ball is tied to both the science and technology development communities to help influence the direction of future missions incl. Decadal Survey.

## Slide 20
Aeolus

## Slide 21: 3D-Winds Data synergy: Wind lidar provides direct wind measurements to anchor wind retrievals from complementary systems
AMVs from imaging and/or sounding instruments
GOES & POES thermal gradient winds
Scatterometry: DWL for vertical extension of surface winds
Mid IR Stereoscopic imaging
  Compact Midwave Imaging System (CMIS, Kelly, APL/JHU)
  Small, lightweight imaging sensors could easily be deployed with a DWL system
  Provide context as well as swath extension of winds for the DWL measurements

## Slide 22: Observations with strongest impacts on forecast
Tropics, impact per observation
Tropics, total impact
Wind measurements have large impacts per observation (especially in the tropics)…
…but there are currently far fewer wind field than mass field measurements.
Observations that include winds (retrieved or measured)
GEOS-5 Impact Summaries: 2017, Tropics

## Slide 23: DWL can measure winds in clouds too

## Slide 24: 2017 Earth Science Decadal Survey Atmospheric Winds
Recognizing the cross-panel importance of the PBL and the challenges of obtaining 3D measurements of horizontal wind, temperature, humidity, and aerosol and trace gases in the PBL, optimal approaches could be:
  To combine Doppler lidar wind profiling with hyperspectral infrared sounding to provide the 3D structure of horizontal wind. This can be further combined with near-surface microwave scatterometer wind over ocean, and ground-based wind profiling, high vertical resolution profiles from radiosondes and commercial aircraft measurements during taking off and landing.
  …
  To bring Doppler Lidar and hyperspectral infrared observations together in a dynamically consistent way through data assimilation and numerical modeling.

## Slide 25: Wind Lidar offers:
Range resolved wind measurement curtains with precise knowledge of measurement height
  Like CALIPSO, the lidar “swath” is vertical – a curtain vs. a carpet
  Adds vertical dimension to swath data
Wind measurements that don’t require features –
  Direct measurement of Doppler frequency shifts in scattered light - no tracking or multiple satellites/revisit time is required
  (for OAWL): SNR is increased with more aerosols (e.g. when clouds are present)
Wind measurements at higher altitudes (molecular channels)
  Same technology used in GrOAWL can be used to measure winds from molecular-only returns
DWL can anchor other measurements

## Slide 26: The Evolution of OAWL
2013 & 2016 ATHENA-OAWL Mission Proposals
2008-2012: OAWL IIP-07
Breadboard system
355 nm only, 4x channels
Single look 12” telescope
Ground validation with NOAA Coherent system
Autonomous flight tests on NASA WB-57
1999-present: Ball design, build and test of OAWL receivers, mission concepts and retrieval/processing algorithms
2012-2015: HOAWL ACT
Breadboard System
Demonstrate 532 nm wavelength channels & depolarization channels
Total 10 channels
HSRL Aerosol retrieval algorithms
2014-2017: HAWC-OAWL IIP
Two look airborne system (build on GrOAWL)
Dual Wavelength + depol. Channels
Athermal interferometer build and demonstration
DC-8 hardware design/build
2015-2017: ATHENA-OAWL Venture-Tech: GrOAWL
Airborne demonstrator System (WB-57)
2-lasers = 400 Hz eff. PRF
4x 532 nm channels
2 looks, 2 telescopes to demonstrate geometry
aerosols
winds
Altitude MSL (m)
Altitude MSL (m)
Since 2003, Ball has worked in a public-private partnership with NASA, NOAA, and weather/wind lidar communities to advance space-based wind lidar technology and fill the global wind measurement gap.