## Slide 1: The NOAA Satellite Observing System Architecture (NSOSA) Study
Frank W. Gallagher III
NOAA / NESDIS / Office System Architecture and Advanced Planning
7 February 2018

## Slide 2: NSOSA Study Background
NOAA Satellite Observing Systems Architecture (NSOSA) study is examining the space segment architecture decisions for space systems post GOES-R/S/T/U and JPSS-1/2/3/4
  Which observation functions should be allocated to which orbits?
  Should we retain the legacy architecture or seek major change?
  Which observation functions should be improved?
Addressing NOAA operational needs, from defined requirements
  Observations that result in warnings, watches, baseline weather and space weather forecasts, and ocean or fisheries actions
Scoped to address NOAA systems, with a knowledge and inclusion of partner contributions and relationships
Intended to result in Pre-Phase-A program activities

## Slide 3: Planning for the Future
Architecture Analysis
Operational Considerations (NOAA/DoD/ Partners)
Strategic Priorities
Technology Opportunities
Policies & Standards
NOAA User Prioritized Requirements
National Weather Service
National Marine Fisheries Service
National Ocean Service
Office of Oceanic and Atmospheric Research
Commercial Engagement
NOAA Ground
Pre-Phase A
Partner Sources
Program(s) of Record
Source Agnostic Data
Instrument Capabilities Allocated to Orbits
Replenishment policies
Cost estimates
Technology roadmap
Notes: Buy, Barter, Build

## Slide 4: Baseline and Timing
2020
2025
2030
2035
2040
2045
2050
GOES
JPSS
DSCOVR/SWFO
MTG
JMA-GEO
EPS-SG / Sentinel
Ocean Altimetry
POR2025
Assumed Partner Continuation
Radarsat
COSMIC
NSOSA Scope
Assume NOAA Enterprise Ground - Including Secure Ingest, etc.
2028
GOES-S Flies Out

## Slide 5: Study Ground Rules
Determine the most cost effective space segment architectures for performing NOAA weather, space weather, and environmental remote sensing (excluding land mapping) missions, beyond the POR to 2050
Priority to Operational NOAA Functions
Launch services provided by NASA KSC Launch Services Program.
Include partnerships (e.g., EUMETSAT, JAXA, CSA)
Team Members
Aerospace Corporation
NASA GSFC
NASA JPL
NASA KSC
SPRWG
JHU APL
MIT-LL
NESDIS - TPIO & OSGS
NESDIS - ACIO

## Slide 6: Goals of the NSOSA Study
Fundamental Goal
  Determine the most cost-effective satellite architecture options for NOAA environmental observation satellites in the post-GOES, post-JPSS era
Related goals
  Identify the big alternatives for the satellite architecture, determine the tradeoff rules. Why do we prefer one major alternative over another? What would drive us one way versus another?
Downstream goals
  Identify the needed next generation programs and when we need to start them
  Lay the ground work for those next generation programs (functions/requirements allocated, trade cases, technology roadmaps)

## Slide 7: Intended Outcomes of Study
Inform choices and opportunities about the next generation constellation architecture to:
  Start pre-formulation in 2019/2020 of next generation programs that must start that early
  Structure follow-on studies to resolve any open issues that can wait
  Identify long-lead investments in technology, so that we can establish funding needs and partner priorities starting in 2018
  Identify any high value partnership changes or opportunities where engagement in 2018 is important
Provide a clear vision/roadmap of the NOAA satellite next generation
Provide rigorous analysis to drive architecture decisions

## Slide 8: Study Methodology
Functions / Goals
NOAA Operational
NOAA Non-Operational (Science)
Enterprise Ground
Software and Hardware capability and capacity
SPRWG
Space Platform Requirements Working Group
NSOSA
Study
Results
High-Value Alternative Architectures
Architectures
Cost Estimates
Integrated Roadmaps
Technology Roadmaps
NOAA Leadership Priorities
Strategic & Cost Goals
Obs Mission Value
Notes: SPRWG Starting point was
NOAA COURL and WMO OSCAR
Enterprise Ground provided the NESDIS ground baseline
Output cost estimates include cost deltas associated with hardward and software changes driven by space architectures

## Slide 9: NSOSA Study Approach
Value Model
Space Platform Requirements Working Group
Instrument Catalog
Constellations Considered
Trade Studies
Performance Evaluation
Integrated Roadmaps
Customer Impacts
General Study Results
Value Model Development
Instrument Catalog Development
Constellation Alternative Synthesis
Score Alternatives
Design and Cost Alternatives
Integration, Trades, Architecture Selection
NSOSA
Study
High-Value Alternative Architectures
Three full architecture cycles enable:
user engagement, learning, fine tuning

## Slide 10: Linking NOAA Requirements to the NESDIS Architecture Study
Value Model expresses relative mission value of performance choices and drives the analysis
NESDIS established a Satellite Platform Requirements Working Group (SPRWG) to work with the study team on this model
  Used NOAA requirements database, NESDIS/TPIO COURL and tools, and WMO OSCAR requirements reference database as a starting point
  Projected needs to 2028 and beyond
  Translated requirements into architecture objectives
  Linked performance choices to requirements satisfaction metrics
Value Model is the basis for mission satisfaction scoring of architecture options

## Slide 11: The EVM (Environmental Data Record (EDR) Value Model)
The EVM is a table listing each objective (sometimes called “requirements”) for NOAA’s space-based observational system of 2030 and beyond, together with the performance attributes of each objective.
A Functional Objective (often just Objective) is something we want to measure-e.g. temperature soundings, a visible image, a solar corona image.
  Group A - Weather, climate, oceans, chemistry objectives
  Group B - Space weather objectives
Group C (Communications Objectives) were handled in a binary sense.
There are also Strategic Objectives, such as assurance of core capabilities (Group D Objectives)
SPRWG focused on Group A and B objectives
NOAA Leadership interleaved and ranked Group A, B, and D objectives collectively

## Slide 12: EVM Capability Levels
Set capability levels for objectives to include:
  Study Threshold (ST): The level at which decreases in capability no longer present a compelling investment, i.e., alternatives with capability below this level will be rejected. Guidelines are no objectives with ST level greater than Program of Record 2025. Some objectives have zero ST performance.
  Expected (EXP): The capability reflecting consensus expectations from the users. Often, but not always, roughly equal to today’s capability.
  Maximum Effective (ME): The level at which increases in capability no longer present a compelling investment (i.e., alternatives with capability above this level will receive no additional credit). Generally a significant improvement over today’s capability.

## Slide 13: Rank Order of Objectives 1-10 in Group A
Ranked in order of improvement from ST to ME.

## Slide 14: EVM Example: Objective A13
A13: 3D Winds (Horizontal Wind in the Troposphere)

## Slide 15: Constellation Analysis
Evaluated nearly 100 different constellations (not all shown here)
All of them met the ST level of performance
Efficient Frontier Curve

## Slide 16: Constellation Analysis – Doppler Wind Lidar (Cycle 3)
Evaluated nearly 100 different constellations (not all shown here)
All of them met the ST level of performance
Non-Zero ST level for 3D winds – ST level met by non-lidar solutions
Many constellations have a Doppler wind lidar as a capability
Cycle 3 Constellations that included a Doppler wind lidar

## Slide 17: Exemplar “Hybrid” Architecture
This is an example architecture that was evaluated as part of the NSOSA analysis.
  Core System
  Hosted GEO Wx imagers E/W (cross-grade from ABI, not equal)
  Government weather-only Center GEO (includes imager+, lightning mapper, in situ SWx)
  Hosted GEO instruments of opportunity
  Comprehensive SWx at L1
  LEO sounders (0530, 1330)
  Commercial user-facing communications
  Data service buys (e.g., GNSS-RO)
  Trade Elements
  Dedicated L5 SWx
  ABI++ capabilities on center GEO – “SuperGOES”
  Doppler wind lidar
  Tundra (polar inclination) with cross-grade ABI and auroral imager – Also covers global weather imaging needs
  1330 LEO Imager
  “Heavy” MW capabilities (e.g. large MW imager)
  Additional Sounders (0530, 1530, crossing, etc.)

## Slide 18: Next Steps for NOAA
Synthesize NSOSA analysis with Decadal Survey analysis
Outreach to industry partners in high interest topic areas
  Instrument approaches to select performance points
  Hosting approaches for sustained constellations
  Potential service demonstrations
Further develop GEO, LEO, SWx, and other long-term roadmaps within NOAA and with partners
  Targeted trade studies within these areas to address specific identified issues
Inform budget development and decision process

## Slide 19: NOAA Space Future Opportunities
NSOSA Study identified opportunities for NOAA to:
  Provide improved capability
  Provide greater agility
  Engage in new business practices
  Do this at a reasonable cost