## Slide 1
Activities at NASA towards 3D wind retrievals from “hyperspectral” IR sounders
Tom Pagano
AIRS Project Manager
Caltech NASA JPL
4800 Oak Grove Dr. Pasadena, Ca 91109
tpagano@jpl.nasa.gov (818) 393-3917
October 13, 2015
© 2015 California Institute of Technology. Government sponsorship acknowledged.
With contributions from
David Santek (UW/SSEC), Kevin Maschhoff (BAE Systems), Will McCarty (NASA GMAO)

## Slide 2: Agenda
Recent developments at NASA related to wind retrievals from IR Sounders
Science and Simulation
  MODIS and AIRS Water Vapor Winds (Santek, SSEC, NASA ROSES)
  Forecast Departures (McCarty, GMAO)
Technologies for IR Sounding
  JPL AIRS and Future Sounding Instruments
  MISTiC Winds (Maschhoff, BAE Systems, NASA IIP)
  CubeSat Infrared Atmospheric Sounder (Pagano, JPL, NASA InVEST)
Call for additional modeling, simulation, technology development, and flight demonstrations

## Slide 3: MODIS Winds have impact to forecast
MODIS Polar Winds Product
AIRS
4 AMSUs
IASI
(Cardinali, ECMWF Tech. Memo. 599, 2009)
MODIS
Winds
MODIS Polar Winds have impact on global 24Hr forecast
MODIS Polar Winds impact in Arctic
https://stratus.ssec.wisc.edu/projects/polarwinds/impacts/impact.html

## Slide 4: AIRS water vapor isosurface shows 3D variability

## Slide 5: AIRS Ozone Hole formation in 3D

## Slide 6: Current Status of 3D Winds from IR Sounders
MODIS 20 July 2012 0551 UTC
Infrared and Water Vapor (including clear sky)
AIRS 20 July 2012 0505 UTC
Ozone: 103 to 201 hPa Moisture: 359 to 616 hPa
by David Santek (UW, SSEC)
Good Impact of AIRS WV Wind per Observation
AIRS winds preliminary evaluation by Will McCarty (NASA/GMAO)
The mean and standard deviation of the observation departures (ms-1)
(Observation minus 6-hr Forecast) for AIRS and MODIS water vapor winds
May to July 2015

## Slide 7
Advance the readiness of a miniature, high resolution, wide field, thermal emission imaging spectrometer to measure vertically resolved tropospheric profiles of temperature and humidity for deriving global 3-D wind measurements.
Provide ~ 2-3 km spatial resolution temperature and humidity soundings of the troposphere using an AIRS-like (Atmospheric Infra-red Sounding) method.
Enable a LEO constellation approach that provides 3-D Wind field measurements and atmospheric state and transport observations at low system cost.
Reduce technology risks with the Infrared Focal Plane Array (IRFPA) and spectrometer technologies critical for significant instrument size, weight and power reduction (20 x 30 x 30 cm, 15 kg, 50 W).
MISTiC Winds: Midwave Infrared Sounding of Temperature and humidity in a Constellation for Winds
Optimize and refine space-based measurement approach based on experience with AIRS, AIRS-Light and small satellite provider experiences.
Demonstrate calibration stability of miniature MWIR spectrometer (4.08 - 5.8 um) in ground testing.
Demonstrate robustness of spectrometer by performing space level thermal fluctuation testing and vibration testing to launch levels.
Verify instrument measurement capability of 3-D cloud-drift and water vapor motion vector winds on high altitude balloon or high-altitude fixed-wing platform.
Demonstrate IRFPA space radiation tolerance (> 25 krad).
Co-Is/Partners: J. Susskind, NASA GSFC; H. Aumann, JPL
TRLin = 4 TRLcurrent = 4
MISTiC Instru-ment will fit on a 27U CubeSat or a ESPA-Class Micro-Sat
IR Sounding
Constellation
Motion
Vector
Winds
Formation
705 km
Orbits,
Sun-Synchronous
Instrument science and payload requirements review 10/14
Instrument science and payload concept review 12/14
Airborne demonstration plan review 06/15
Detector/ROIC radiation test/analysis complete 09/15
Calibration stability test complete 03/16
Airborne instrument design/build complete 05/16
Airborne demonstration complete 10/16
Airborne demonstration data analysis complete 12/16
IIP-13-0004
PI: Kevin R. Maschhoff, BAE Systems

## Slide 8: Infrared Sounding at JPL
From Cardinali (ECMWF Tech. Memo. 599, 2009)
AIRS
Ongoing IR Sounder Projects at JPL
  AIRS/AMSU: Instrument Operations, Calibration, Product Development and Validation. Aqua Retires 2022
  SIPS (CrIMSS): L2/L3 Product Development, Cross-Calibration, and Validation. Climate Data Record Continuity
  Cutting Edge Research: Retrieval Development, Water Vapor Transport, Climate Model Validation, Cloud Properties, LES Models, Instrument Simulation, OSSE’s
  R2O: AIRS V5 Retrieval basis of NUCAPS. For AWIPS-II
JPL Technologies Support Next-Gen IR Sounders
  HotBIRD Infrared Detector Materials
  Advanced Cryocooler Characterization Lab
  Advanced IR Grating Spectrometer Developments
  CubeSat Development Laboratory
Many options for Next-Gen IR sounders
  1km LEO: MIRIS: IR Sounder w/ VIIRS IR Imaging. Full Swath, Full Spectral Range. Post-JPSS, NOAA
  3km - 13.5km LEO: CIRAS 6U CubeSat: Tech Demo for NASA InVEST. NOAA Study for EON-IR (Follow-on to CIRAS)
  5km GEO: SIRAS. Full Spectral Range, Hosted Payload
  100m LEO: Boundary Layer Processes Sounder. Narrow (100km) swath, pointable for special events
JPL/BAE AIRS
JPL Sounding Products Support Weather, Climate and Atmospheric Composition Research
HotBIRD MWIR Detectors
RTD Wide-Field Grating Spectrometers
OCO-2 Spectrometers
Moderate Resolution Infrared Imaging Spectrometer (MIRIS)

## Slide 9
Micro Pulse Tube Cryocooler (Lockheed Martin)
JPL HOT-BIRD Detector
CubeSat Infrared Atmospheric Sounder (CIRAS)
For NASA InVEST
PI: Tom Pagano (JPL)
Sponsor: NASA ESTO
JPL GRISM Spectrometer
CIRAS Technologies
CIRAS
CIRAS Mission
Demonstrate Key Technologies needed for Infrared Instruments on CubeSats
Demonstrate fidelity of Hyperspectral Mid IR radiance measurements to retrieve Temperature and Water Vapor Profiles
Fill Coverage Gaps and Improve Timeliness of Operational IR Sounders
TRL in: 5-6, TRL out: 7
Build: 2016, 2017. Launch 2018 (TBD)
Parameter | CIRAS
Spatial | 
Orbit Altitude | 600-850 km
Scan Range | 0.84° - 57°
Horizontal Res’n | 1.6 km - 13.5 km
Spectral | 
Method | Grating
Band 1 | 4.78-5.09 µm
Res’n / Sampling | 0.5 / 0.2 cm-1
Total Channels | 625
Radiometric | 
NEdT (@250K) | <0.25 K
Resources | 
Size | 6U Cubesat
Mass | 8.5
Power | 37.5
Data Rate | 2 Mbps
CIRAS Measurements
Lower Tropospheric Temperature Profiles
Lower Tropospheric Water Vapor Profiles
Goal: Experimental Demonstration of 3D Winds
CIRAS will significantly reduce the cost of atmospheric sounding in the infrared and enable improved timeliness through constellations
© 2015 California Institute of Technology. Government sponsorship acknowledged.
*Patent Pending

## Slide 10: CIRAS can demonstrate higher spatial resolution hyperspectral IR sounding
18 km
63 km
225 km
2200 km
CIRAS bins pixels and multiple frames while scanning to achieve desired spatial resolution
Pixel binning scheme and scan rate are programmable while in orbit
Native resolution of CIRAS is 0.8 km
Changing scan range (and rate) and pixel binning can improve spatial resolution at the expense of coverage (see right)
CIRAS limited due to cost, but future instruments can have wider swath
Fixed NEdT @ <0.25K
AIRS, CrIS, IASI, and CIRAS Requirement
For Winds

## Slide 11: Method Developed using AIRS Linear Retrievals and STK to Simulate Sounder Data
RMS Temperature Error (K) between Simulation and Nature Run
T.S. Pagano, W. Mathews, F. Irion, E. Sturm, “Simulating satellite infrared sounding retrievals in support of observing system simulation experiments (OSSEs)”, Proc. SPIE 9222, San Diego, CA (2014); doi: 10.1117/12.2061468
Nature run profile sampled by AIRS, ARIES, GEO scan pattern and footprint
fT,i = a T,i + b T,i ln (p_cld) + … c T,i (f_cld), i = 1 to 23
Similar for water vapor with add’l q_tot
Linear retrieval to simulate AIRS
Averaging Kernel and Cloud Dependence from Real AIRS Data
Objective
Provide simulated temperature and water vapor retrievals from Hurricane Nature run
Method
Satellite Took Kit Mapping, Footprint Binning: AIRS (13.5 km), CIRAS (3 km), GEO (5km)
Linear Retrieval based on AIRS Performance
Results
AK’s for CIRAS 2x Higher than AIRS (Less Cloud Effect)
Results sent to Bob Atlas at AOML for Assimilation Impact Studies. Results show short term (< 12 hr) improvement.
Method can be used to simulate wind data

## Slide 12: Summary and Recommendations
Measurements of winds in 2D using water vapor features now possible with polar orbiting and GEO imagers.
  Provides valuable data to forecasters, particularly in northern latitudes
  Accuracy impacted by variability in 3rd (z) dimension.
  Since imagers not designed for winds, the coverage is limited to polar regions (polar orbiters), or GEO FOR
Winds measurement using current IR sounders has been demonstrated
  AIRS in polar regions. CrIS and IASI in process
  Coarse spatial resolution of current IR polar sounders limit wind speed accuracy
NASA supporting 3D winds using hyperspectral IR Sounding
  Retrievals from AIRS and assimilation testing
  Technology development (MISTiC Winds and CIRAS)
Several issues remain for hyperspectral IR Sounders
  Cloud interference
  Feature coherence
  Retrieval accuracy (especially over land and with Mid-IR)
  Cost of GEO or LEO Constellation
Recommended Multi-agency Activities
  Development of a multi-agency forward model for the Midwave IR
  IR sounder wind-retrieval simulations
  OSSE’s to determine forecast impact of IR sounder winds
  Assimilation impact studies using Midwave IR from IASI
  Additional technology development
  Additional airborne and spaceflight demonstrations