## Slide 1: Observing system simulation experiment (OSSE) for future space-based Doppler wind lidar in Japan
Kozo Okamoto1,2
T. Ishibashi1, S. Ishii2, P. Baron2, K. Gamo3, T. Tanaka1, T. Kubota4
1: JMA/MRI, 2:NICT
3:FUJITSU FIP corporation, 4:JAXA
Working Group Meeting on Space-based Lidar Winds Meeting 21-23 March 2017, Newport News Marriott at City Center, VA, USA
JMA/MRI : Japan Meteorological Agency / Meteorological Research Institute
NICT : National Institute of Information and Communications Technology
JAXA : Japan Aerospace Exploration Agency

## Slide 2: Content
1. Motivation and purpose
2. Method
  OSSE
  Lidar simulator
  Data assimilation
3. Results of assimilation experiments
4. Summary and plans

## Slide 3: 1. Motivation and purpose
Global wind profile observations are essential to NWP but is not sufficient in the current observing system
Space-based Doppler wind lidar (DWL) is one of promising candidate to fill the gap
Purpose of this OSSE study:
  Assess impacts of DWL on NWP
  Investigate DWL configuration to achieve better outcomes
  Prepare for operational use of ADM-Aeolus and future DWL in the data assimilation system

## Slide 4: Plans of Japanese DWL and satellite
DWL
  Coherent detection
  2 azimuthal direction (45, 135 deg), 35 deg off-nadir
  Horizontal res: 100 km
Satellite
  Super-low altitude satellites (altitude~220km)
    Relax requirement of pulse energy and telescope size
Under discussion
  Satellite orbit : Polar or low-inclination (Tropical)
  Specific lidar parameters: resolution,,,
  Better data assimilation settings: observation error, QC,,,
@JAXA/SLATS
Altitude (km) | V. Res. (km) | Accuracy (m/s)
8~20 | 2 | 5
3~8 | 1 | 3
0~3 | 0.5 | 1
Notes: Coherent detection lidar can be downsized more easily than direct detection lidar.
This enhance the affinity with the satellite system we are discussing.
This has a close affinity with the satellite system

## Slide 5
1. Motivation and purpose
2. Method
  OSSE
  Lidar simulator
  Data assimilation
3. Results of assimilation experiments
4. Summary and plans

## Slide 6: OSSE
SOSE: Sensitivity Observing System Experiment (Marseille et al. 2008)
  Pseudo-truth (PT) field is created by correcting first-guess based on adjoint sensitivity and assimilating real observations
    PT field is consistent with obs and reduces forecast-errors
  Not need to simule existing observations
Lidar simulator: ISOSIM-L
  the Integrated Satellite Observation SIMulator for a spaceborne coherent Doppler lidar
  Calculate LOS wind speed and quality information from atmospheric field (e.g. winds), clouds and aerosols based on a maximum likelihood probability approach
Hourly Aerosol field
  Generated with global aerosol model (MASINGAR) constrained by the PT winds
Notes: Full-scale (fully developed) model

## Slide 7: OSSE flow
SOSE PT
cloud
Lidar simulator (ISOSIM-L)
Simulated WLOS
aerosol model
DWL wind simulation (off-line)
wind
aerosol
Existing observation
Simulated WLOS
assimilation
first guess
analysis
forecast model
assimilation
first guess
data assimilation cycle
PT: Pseudo-Truth
WLOS: LOS wind speed

## Slide 8: Data assimilation
Assimilate LOS (line of sight) wind
  Observation operator : WLOS = -(u*sinφ + v*cosφ)*sinθ
QC
  Anomalous QC: reject data at the lowest layer and with ISOSIM-flag
  SNR-QC: reject data with small signal (N1/2SNR<0.1)
    N: total range-bin number in a resolved volume
  Gross error QC: reject data with large firstguess departure
    |OBS-FG|>0.5m/s (Z<3km), 1.0 (3<Z<8) and 1.5 (Z>8)
Observation error R
  Emes: measurement error, estimated by ISOSIM-L
  Eope: observation operator error, Erep: representativeness error
     assumed Eope2 + Erep2 = 1.0
  C: inflation factor  set to 4.0 in |lat|<60deg, 6.0 otherwise

## Slide 9: Simulated DWL data (around 11.4km)
09 ~ 15 UTC on August 1.
All
Polar Orbit
Tropical Orbit
QC passed
Log(N1/2SNR)

## Slide 10: Number of used and QC-failed DWL at each analysis
15 % data pass all the QC
SNR-QC plays biggest role in rejection (64%)
Chart: 
| use | Anomalous | SNR | Gross
Polar1 | 10513 | 6728 | 40536 | 6023
Tropical1 | 9615 | 6733 | 41363 | 6096
Polar8 | 8954 | 6728 | 39759 | 8362
Tropical8 | 10111 | 6734 | 39629 | 7344
Notes: use
Anomaly
SNR
Gross
Polar1
10513
6728
40536
6023
TRMM1
9615
6733
41363
6096
Polar8
8954
6728
39759
8362
TRMM8
10111
6734
39629
7344

## Slide 11: PDF of OBS-PT before/after QC (2 Jan and Aug 2010)
QC successfully reject data with large obs-PT
Data quality is better in Jan than in Aug.

## Slide 12
1. Motivation and purpose
2. Method
  OSSE
  Lidar simulator
  Data assimilation
3. Results of assimilation experiments
4. Summary and plans

## Slide 13: Data assimilation experiments
Low-res version of operational global DA system of JMA as of 2010.
  6-h cycle, incremental 4D-Var, H.res=60km/120km
Data assimilated
  Control exp. (CNTL) : full operational data set
  Test exp. CNTL + DWL LOS wind profiles
    TestP : DWL on a polar satellite
    TestT : DWL on a tropical satellite
Experiment period
  Winter exp. 20 Dec 2009 – 9 Feb 2010 (DWL assimilation:1 – 31 Jan)
  Summer exp. 20 Jul – 9 Sep 2010 (DWL assimilation:1 – 31 Aug)

## Slide 14: Monthly, zonally accumulated number
Summer exp.
90S
90N
1000
100
500
90S
90N
1000
100
500
TestP
TestT
90S
90N
1000
100
500
90S
90N
1000
100
500
Winter exp.
1-31 Jan. 2010
1-31 Aug. 2010

## Slide 15: Monthly, zonally accumulated number
1-31 Jan. 2010
1-31 Aug. 2010
Summer exp.
90S
90N
1000
100
500
90S
90N
1000
100
500
TestP
AMV
90S
90N
1000
100
500
90S
90N
1000
100
500
Winter exp.
AMV in summer exp.
AMV in winter exp.
90S
90N
1000
100
500
90S
90N
1000
100
500
Notes: the lack of vertical variability of cloud and aerosol
due to relatively poor vertical model resolution
in comparison with the vertical bin width
when ISOSIM-L retrieves DWL winds over the fixed altitude ranges

## Slide 16: Forecast scores of U in winter exp.
Relative RMS forecast error reduction (%)
Obvious improvement in wide regions and forecast ranges
TestP
NH
SH
TR
degrade   improve
24
48
72
120
96
144
168
0
1000
forecast [h]
100
24
48
72
120
96
144
168
0
1000
forecast [h]
100
24
48
72
120
96
144
168
0
1000
forecast [h]
100
TestT

## Slide 17: Forecast scores of U in summer exp.
Generally positive, but negative in some regions and forecast ranges
TestP
NH
SH
TR
24
48
72
120
96
144
168
0
1000
forecast [h]
100
24
48
72
120
96
144
168
0
1000
forecast [h]
100
24
48
72
120
96
144
168
0
1000
forecast [h]
100
TestT
degrade   improve
Notes: Contaminated with bad quality data
There is still room to improve [develop more appropriate] obs error and QC criteria.

## Slide 18: Typhoon track forecast errors
Position errors (km) as a function of forecast hours up to 84-h
Slightly positive impact for both experiments

## Slide 19: Example of typhoon track forecast
Track forecasts of TC DIANMU (T1004)
TestP
TestT
Cntl
Test
Besttrack

## Slide 20: Comparison of TestT and TestP
Relative improvement of U
Mixed results  hard to say which is better!
Winter
NH
TR
24
48
72
120
96
144
168
0
1000
forecast [h]
100
24
48
72
120
96
144
168
0
1000
forecast [h]
100
24
48
72
120
96
144
168
0
1000
forecast [h]
100
TestP +ve   TestT +ve
SH
Summer

## Slide 21: 4. Summary and Plans
OSSE system for space-borne DWL has been developed
  SOSE-based OSSE
  Produce hourly aerosol filed that is consistent with PT wind
  End-to-end simulator ISOSIM-L calculates LOS wind and quality information
  Develop QC and observation error based on the quality information
Preliminary results of one-month assimilation experiments
  Assess impacts of DWL onboard polar and tropical satellites in winter and summer (Jan and Aug 2010)
  Generally positive impacts of DWL, either polar or tropical satellite
  Winter experiment show better forecast skills than summer experiment
  Unclear superiority of polar and tropical DWLs
    Tropical DWL is superior to polar DWL in short-range forecast but inferior later
  Typhoon track forecast is slightly improved
Plans
  Test various configuration of DWL and assimilation system
    Data coverage, resolution
    QC, thinning, observation error, different OSSE approach (e.g. NR-OSSE)
  Investigate complementary benefits of DWL and other winds (e.g. AMVs)

## Slide 22: References
Baron et al. 2017: Feasibility study for future space-borne coherent Doppler wind lidar, Part 2: measurement simulation algorithms and retrieval error characterization. Under revision for J. Meterol. Soc. Japan.
Ishii et al., 2016: Measurement performance assessment of future space-borne Doppler wind lidar. SOLA, 12, 55-59.
Ishii et al. 2017: Feasibility study for future spaceborne coherent doppler wind lidar, Part 1: Global Wind Profile Observing System. Under revision for the J. Meteor. Soc. Japan.
Okamoto et al. 2107:Feasibility study for future Space-borne Coherent Doppler Wind Lidar, Part 3: Initial evaluation using the Operational Global Data Assimilation System. In preperation

## Slide 23: Supplemental slides

## Slide 24: Observation error (after inflation)
Monthly zonalmean average

## Slide 25: Forecast improvement against own analysis
Normalized RMSE difference
  (RMSECNTL-RMSETEST)/RMSECNTL
  +ve shows improvement. Statistically significance is indicated by circles
Short range wind forecast is improved especially for lower tropospheric wind in the tropics
  TestT experiment shows slightly greater improvement
Improve
Degrade
Forecast hours (~216h)
0 72 144 216
0 72 144 216
0 72 144 216
0 72 144 216
0 72 144 216
Psea
T850
Z500
Wsp850
Wsp250
0 72 144 216
0 72 144 216
0 72 144 216
0 72 144 216
0 72 144 216
Psea
T850
Z500
Wsp850
Wsp250
TestP
TestT