## Slide 1: DAWN Contributions to Investigating Arctic Atmospheric Dynamics and Numerical Model Validation
S. Greco, G.D. Emmitt, A.K. DuVivier, and M. Kavaya
Simpson Weather Associates
University of Colorado - CIRES
NASA LaRC
Working Group Meeting on Space-based Lidar Winds
Newport News, VA
March 21 2017

## Slide 2: NASA’s PolarWinds
NASA funded two airborne Doppler Wind Lidar campaigns:
  Campaign 1 Oct-Nov 2014 on NASA UC-12B King Air based Kangerlussuaq, Greenland
  Campaign 2 May 2015 on NASA DC-8 based
  Keflavik, Iceland
Over 80 hours of research flights in the Arctic region near Greenland and Iceland
Purpose was to conduct basic polar science investigations and demonstrate DWL technology readiness for ADM Cal/Val
Included Co-flights (six) with high-altitude DLR Falcon with DWL

## Slide 3: PolarWinds Science Objectives
Validate numerical model forecasts (WRF, P-WRF) and reanalysis (ASR, ERA) characterizations of airflow in the lower atmosphere over the open oceans, land, ice sheets and transition zones
Conduct detailed investigations into dynamic features such as Arctic low level jets (Tip Jet), barrier winds and OLEs.
Characterize and study the wind regime of the lower atmosphere over marginal ice zones in the Arctic
Provide wind/aerosol observations to validate or compare with existing remote sensing platforms
- CALIPSO aerosol measurements
  - MODIS Atmospheric Motion Vectors
  - ASCAT Ocean Vector Winds

## Slide 4: Instruments and Models
DAWN (Doppler Aerosol WiNd lidar)
- Coherent detection lidar (aerosol)
- Downward pointing scanner
- 2-12 Scanning angles (mostly 2 and 5)
Yankee Environment (YES) Dropsondes
- Campaign 2 – almost 90 dropsondes
OSU Polar WRF run operationally twice daily
University of Colorado WRF for research

## Slide 5
DAWN on board the NASA King Air 12-C (11/2014)
and NASA DC-8 (May 2015)

## Slide 6
Attribute | Value
Airplanes Flown | DC-8 and UC-12B
Solid-State Laser Crystal and Wavelength | Ho:Tm:LuLiF, 2.053472 Microns
Laser Pulse Energy E, Rate f, FWHM Duration t | 250 mJ, 10 Hz, 180 ns
Pointing Knowledge Technique | Dedicated INS/GPS on Lidar
LOS Wind Measurement Precision | < 1 m/s
u, v, w Measurement Precision | < 1 m/s
Horizontal Resolution of Full Vertical Profile | 2-7 km
Vertical Resolution of Full Vertical Profile | 75 – 150m
DAWN

## Slide 7: DAWN Performance and Data
While DAWN performed less than ideally due to misalignments and sensitivity issues (see Emmitt and Henderson talks), the DAWN profiles demonstrated close agreement with Dropsondes
Post processing for optimum data set removed ground and aircraft effects
Final DAWN data have provided quality data for numerical model (e.g. Polar WRF) validation and for the scientic study of atmospheric circulations such as LLJs and Upper Jets.

## Slide 8
Polar Winds DAWN-Dropsonde Comparison – 5 Days (35 Drops)

## Slide 9
Height Layer | Number of Comparisons | ∆z (m) | DAWN –Drop (m/sec) Mean ∆WS | DAWN – Drop (m/sec) Mean ABS(∆WS) | DAWN – Drop (deg) Mean ∆WD | DAWN – Drop (deg) Mean ABS(∆WD) | RMSE DAWN -Drop ∆WS
ALL | 468 | 1.97 | -0.004 | 1.15 | -1.75 | 9.11 | 2.28
5200 – 4000 m | 87 | 2.28 | 0.13 | 1.06 | -7.80 | 13.81 | 1.87
4-3000 m | 92 | 2.21 | 0.26 | 1.28 | 0.8 | 13.28 | 2.94
3-2000 m | 92 | 1.92 | -0.005 | 0.92 | -1.95 | 11.33 | 1.32
2-1000 m | 133 | 1.74 | 0.108 | 1.14 | -0.27 | 4.70 | 2.03
1000m – sfc | 64 | 1.73 | -0.815 | 1.52 | 0.084 | 2.67 | 3.81
DAWN-Dropsonde Comparison for May 21, 2015 mission including 8 dropsondes

## Slide 10
- 274 x 324 one-domain grid with 8 km spacing
- 48 layers: Lowest levels at 7 and 14 m; 8 layers at lowest 500 m;
- 60-sec time step; run with 20 tasks; 48-hr runs; output every 3 hr
- Morrison 2-moment microphysics
- RRTMG longwave and shortwave radiation
- MYJ Planetary boundary layer and surface boundary layer
Noah Land surface model
Fractional sea ice 1.5 m thick; albedo 0.82; 5 cm snow on sea ice
- Run TWICE a day with 00 & 12 UTC as its initial times
- IC and BC interpolated from the daily (00, 12Z) NCEP GFS
Polar Winds Model Specifications WRF 3.6.1 with OSU BPCRC polar optimizations (Polar WRF)

## Slide 11
Polar Winds North Atlantic/Greenland Grid
Polar WRF 3.6.1 274 x 324 Points Δx = 8 km
Summit
Thule
Aasiaat
Sisimiut
Iqaluit
Tasiilaq
Narsaq
Qeqertarsuaq
Nuuq
Kangerlussaq

## Slide 12
PolarWinds
Campaign I
Flight Tracks
Greenland

## Slide 13
PolarWinds
Campaign II
Flight Tracks
Greenland

## Slide 14: May 21, 2015 – Barrier Wind Study Intercomparison of DAWN, Dropsondes and WRF

## Slide 15
L
Pressure builds up along Coast
Wind
Barrier Wind
Figure from: Doyle and Shapiro (1999)
Note: The vertical and horizontal dimensions are not equal scales
Greenland is a barrier to cyclone circulation.
(11,000 ft.)
Notes: Very sharp jump from sea level to high elevation. Cold air can’t rise over the terrain.
Topography changes local pressure fields: this alters the winds
Air comes shooting off the tip after the barrier flow -> tip jet
Very basic dynamics

## Slide 17: Colorado WRF V3.7.1 – Summary of Model Runs
50, 25, 10, 5 km grid spacing (no nesting) over same domain
40 and 60 vertical Levels
MYNN2.5 and UW Boundary Layer Schemes
Sea ice thickness = 0.5m
RRTMG shortwave and longwave radiation
Kain-Fritsch cumulus
Morrison microphysics
Revised MM5 surface layer
Notes: WRF: high res marginally better and more vertical levels marginally better.

## Slide 18
ASCAT
ASCAT
WRF-5KM
WRF-5KM

## Slide 19: DAWN/dropsonde comparisons in highly varying coastal region:Greenland East Coast Barrier Wind Case
Red circles:
DAWN profiles
Yellow stars:
Dropsondes

## Slide 20
Greenland terrain
Notes: Two campaigns: compare to obs. Look at satellite data from those times too. Note: surface scatterometers can’t capture winds along coast because of sea ice there.

## Slide 21
D2
Off Coast

## Slide 22
D3
Near Coast

## Slide 23
D4
Off Coast

## Slide 24
D5
Near Coast

## Slide 25
Greenland terrain
D
F
Notes: Two campaigns: compare to obs. Look at satellite data from those times too. Note: surface scatterometers can’t capture winds along coast because of sea ice there.

## Slide 30: Barrier Winds Summary
DAWN wind profiles closely match dropsondes
DAWN and dropsondes show stronger narrower jet near the coast but a broader/deeper and slightly weaker wind max further off the coast
Higher horizontal and vertical resolution model runs better capture jet winds
Higher vertical resolution run is needed to capture DAWN observed jet structure but WRF still misses speed gradients and variability
Choice of BL scheme made little difference
DuVivier et al., (2017) – complete model study ACCEPTED for publication in MWR

## Slide 31
October 31, 2014– Tip Jet Study Intercomparison of DAWN and OSU Polar WRF

## Slide 32
Very similar to the easterly tip jet studied by Renfrew et al., 2009 (QJRMS)

## Slide 35
All sections of complete
Profiles below 1-1.2 km

## Slide 36
Stronger winds Near Tip
Section 1

## Slide 37
Weaker winds SW of TIP

## Slide 38
6
3
1
Acceleration near tip

## Slide 39
6
1
3
Veering around tip
Separation of flow layers

## Slide 41
5
4
Acceleration and deepening near tip
Deceleration moving west
of Tip

## Slide 42
5
4

## Slide 43
Polar WRF
Polar WRF 3.6.1 274 x 324 Points Δx = 8 km
Summit
Thule
Aasiaat
Sisimiut
Iqaluit
Tasiilaq
Narsaq
Qeqertarsuaq
Nuuq
Kangerlussaq

## Slide 45
Section 2

## Slide 46
Section 4

## Slide 47
Section 5

## Slide 48: Tip Jet Summary
OSU WRF does decent job in forecasting the wind speeds near the tip
BL scheme chosen for PolarWRF results in very smooth and unchanging winds over significant layers and does not capture the variability in the DAWN profiles
WRF does not seem to capture the veering of the wind “around” the tip
Unfortunate that DAWN was unable to produce measurements above 1200-1300m

## Slide 49
May 19, 2015– Upper Jet Study
Co-Flight with DLR Falcon Intercomparison of DAWN and Dropsondes

## Slide 50
SURFACE

## Slide 51
~ 8 km

## Slide 56
1336z
180

## Slide 57
1359z
225

## Slide 58
1410z
250

## Slide 59: Current and Future Work
Complete model validation for current and futures cases
Complete DAWN-Dropsonde comparisons
Processing and archival of all data
Scientific investigations of:
    Katabatic flows
    OLEs
    Low-level flow over Marginal Ice Zone