## Slide 1: The Simulation of Doppler Wind Lidar Observations in Preparation for ESA’s Aeolus Mission Will McCarty NASA/Goddard Space Flight Center Global Modeling and Assimilation Office R. Errico, R. Yang, R. Gelaro, M. Rienecker

## Slide 2: ESA Aeolus
Direct-Detection technique (355 nm)
  Vertical single-component profiles in clear sky (Rayleigh)
  Higher quality measurements in presence of scattering agent (Mie)
Orbit Characteristics
  408 km
  Dawn-dusk
  Sun-synchronous
Viewing Geometry/Sampling
  90° off-track (away from sun)
  35 ° off-nadir
  Continuous sampling @ 50 Hz

## Slide 3: ADM-Aeolus Pre-Launch Preparedness
Realistic Proxy Data - No spaceborne heritage, must simulate observations
Utilize OSSE framework
  Joint OSSE Nature Run (ECMWF, T511)
  Existing observing system developed in-house at GMAO (R. Errico)
    conventional and remotely-sensed observations
  Simulate ADM observations
    Lidar Performance Analysis Simulator (LIPAS), via KNMI (G.-J. Marseille & A. Stoffelen)
    Need proper sampling (spatial & vertical), yield, and error characteristics
  Not intended to sell Aeolus (already sold)

## Slide 4: What is an OSSE
Time
Analysis
Analysis
Analysis
Analysis
Analysis
Analysis
Real Evolving Atmosphere, with imperfect observations. Truth unknown
Climate simulation, with simulated imperfect “observations.” Truth known.
Observing System Simulation Experiment
Assimilation of Real Data

## Slide 5: Simulating Observations
Six million+ observations are assimilated globally, daily
  Most observations are from satellites
A successful OSSE requires realistic fake observations
Figure via ECMWF

## Slide 6: Clouds in the Joint OSSE Nature Run
Importance of clouds
  The top of a cloud can act as a scattering agent
  Optically thick clouds limit wind retrievals
Placement of clouds
  Realistic vertical placement of clouds
  NR underestimates cloud amount
    ~12% globally
    Related to measurement yield
NR Under-Represents clouds
NR Over-Represents clouds
DJF Cloud Fraction Difference
(NR – CloudSat/CALIPSO)
Improper Cloud Representation…
…Improper Observation Yield & Quality

## Slide 7: Observation Simulation
Lidar Performance Analysis Simulator (LIPAS)
Single-LOS observations generated from NR
  Meteorology from NR
  Clouds from NR w/ maximum-random overlap
  Aerosols from GOCART replay forced by NR Meteorology

## Slide 8: Observation Simulation
Lidar Performance Analysis Simulator (LIPAS)
Single-LOS observations generated from NR
  Meteorology from NR
  Clouds from NR w/ maximum-random overlap
  Aerosols from GOCART replay forced by NR Meteorology

## Slide 9: Assimilation Results
All results shown are from January of Joint OSSE Nature Run
  0000 and 1200 UTC analyses only
Control experiment include conventional & remotely sensed observation simulated from Nature Run
  Radiances include TOVS/ATOVS, AIRS
  Remotely sensed atmospheric winds from Atmospheric Motion Vectors (AMVs)
Experiments:
  DWL – Both Rayleigh and Mie observations
  RAY – Rayleigh only
  MIE – Mie only

## Slide 10: Assimilation Results
Results shown are in terms of reduction of RMS relative to the Nature Run Truth:
  δRMS = RMS(DWL – Truth) – RMS(CTL – Truth)
    If δRMS < 0, RMS is reduced by adding DWL observation, or the analysis is improved relative to the NR truth
    If δRMS > 0, RMS is increased by adding DWL observations, or the analysis is degraded relative to the NR truth

## Slide 11: Assimilation Results
Large reductions of RMS seen over tropics
Existing Observations primarily of mass field (passive satellite radiances)
Winds cannot be inferred through balance assumptions
Zonal Wind RMS Difference (ms-1)
Reduction in RMS by adding DWL
Increase in RMS
by adding DWL

## Slide 12: Assimilation Results
Reductions also seen in meridional wind field
At equator, single-LOS obs are nearly u (~83º from due-north @ equator)
Meridional Wind RMS Difference (ms-1)
Reduction in RMS by adding DWL
Increase in RMS
by adding DWL

## Slide 13: Assimilation Results
Zonal Wind RMS Difference (ms-1)
Reduction in RMS by adding DWL
Increase in RMS
by adding DWL
Smaller contour intervals show mostly positive in both N. & S. hemispheres
Evidence of satellite tracks
  Less in data-rich N. Hemisphere
  00/12 UTC Sondes

## Slide 14: Assimilation Results
Impact at 200 hPa consistent through troposphere
Less impact towards surface
  Less observations
  Increased contamination
Lesser impacts in N./S. hemispheres
  Winds through mass-wind balance
Tropics (-30º to 30º)
NH Extratropics (30º to 90º)
SH Extratropics (-90º to -30º)

## Slide 15: Assimilation Results
Relative humidity similar to winds
Largest impacts again seen in Tropics
The improved characterization of the winds improves the transport of moisture
  No balance between moisture/winds in analysis procedure
Tropics (-30º to 30º)
NH Extratropics (30º to 90º)
SH Extratropics (-90º to -30º)
Tropics (-30º to 30º)
NH (30º to 90º)
SH (-90º to -30º)

## Slide 16: Assimilation Results
Improvement less uniform, but still dominant signal
Relative Humidity RMS Difference (%)

## Slide 17: Assimilation Results
Larger impact from Rayleigh Obs
  ~3x More Observations aloft
  Rayleigh obs error characteristics more predictable
  Mie positive in tropics, neutral in extratropics
Zonal Wind RMS Difference (ms-1)
DWL (Rayleigh + Mie)
Mie Only

## Slide 18: Assimilation Results
Larger impact from Rayleigh Obs
  ~3x More Observations aloft
  Rayleigh obs error characteristics more predictable
  Mie positive in tropics, neutral in extratropics
Zonal Wind RMS Difference (ms-1)
DWL (Rayleigh + Mie)
Rayleigh Only

## Slide 19: Assimilation Results
Larger impact from Rayleigh Obs
  ~3x More Observations aloft
  Rayleigh obs error characteristics more predictable
  Mie positive in tropics, neutral in extratropics
DWL (Both)
Rayleigh Only
Mie Only

## Slide 20: Assimilation Results
Chart: Pressure Bin (hPa)
| 900-1000 | 800-900 | 600-800 | 400-600 | 300-400 | 250-300 | 200-250 | 150-200 | 100-150 | 50-100
Mie | 2.6476 | 2.3794 | 2.7699 | 3.0397 | 3.1445 | 3.2585 | 3.2934 | 3.5367 | 3.8014 | 3.9845
Rayleigh | 5.0166 | 4.6547 | 4.0256 | 3.8797 | 3.7764 | 3.6159 | 3.4322 | 3.5119 | 3.4008 | 3.1308
Chart: Count (Full Month)
| 900-1000 | 800-900 | 600-800 | 400-600 | 300-400 | 250-300 | 200-250 | 150-200 | 100-150 | 50-100
Mie | 47005 | 60665 | 72929 | 74513 | 51981 | 34663 | 37053 | 38233 | 25526 | 19131
Rayleigh | 35464 | 38658 | 117479 | 170388 | 126783 | 86321 | 88260 | 120197 | 158064 | 159174
200 hPa
850 hPa

## Slide 21: Assimilation Results
At 850 hPa, impacts are more similar w/ two observation types
RAY
MIE
DWL
Zonal Wind RMS Difference (ms-1)

## Slide 22: Conclusions, Caveats, and Future Efforts
These results are overstated!
  Error in simulated DWL observations inherently understated
    No added representativeness error, engineering change from Burst Mode to Continuous Mode
  Error in Yield
    Lack of clouds in NR not accounted for in DWL obs simulation
Forecast height anomaly scores improved, though not beyond 95% significance for sample size
Shows expected result that largest impact is expected in tropics
Future work
  Include incorporation of L2B processing into DA System (GSI)
  Redo experiment w/ simulator updated for continuous mode ops

## Slide 24: Assimilation Results
Similar impact from both obs types
  Counts similar
  Sampling issue near Antarctic
  Mie potentially slightly improved in tropics
DWL (Both)
Rayleigh Only
Mie Only