## Slide 1: Updates on Single Frequency 2 µm Laser Sources
Timothy Shuman
Laser Scientist
Fibertek, Inc.
Program Manager: Floyd Hovis

## Slide 2: Acknowledgements
FIBERTEK
Kevin Andes
Ti Chuang
Joel Edelman
Joe Rudd
Tom Schum
NASA LANGLEY RESEARCH CENTER
Jirong Yu
Mulugeta Petros
Upendra Singh

## Slide 3: Outline
Motivation for 2 µm laser sources
2 µm Risk Reduction Laser Transmitter (RRLT)
  Program overview
  Key design features
  Latest results
2 µm single frequency CW seed laser overview
Summary

## Slide 4: Motivation
Airborne and space-based wind measurements are needed:
  Critical to improving global weather forecasting and weather hazard warnings
  Important to climate change research
2 µm sources are used in the coherent channel of hybrid wind systems
  Determined the optimum system to perform these measurements
Requires not only hardened high energy pulsed lasers but also hardened CW lasers to seed them for single frequency operation

## Slide 5: 2 µm Risk reduction laser transmitter (rrlt) for airborne & space-based doppler wind lidar

## Slide 6: Program Background
NASA, NOAA and the DoD all have been pursuing global wind measurements since the 1970s
  A hybrid system utilizing coherent and direct detection is optimum
  The coherent channel needs a high energy pulsed 2 µm laser source
NASA LaRC successfully advanced 2 µm laser technology from 20 mJ to 1.2 J per pulse by Dec. 2005 via internal funding
Purpose of this program to build a risk reduction laser incorporating all of LaRC’s lessons learned in an engineered “space-like” breadboard (TRL 6)
  Understand laser behavior
  Demonstrate the shot lifetime needed for space
  Meet the performance required for a hybrid wind LIDAR system
Phase 3 SBIR cost sharing program with funding split between NASA LaRC and Fibertek

## Slide 7: Performance Targets
Parameter | Value
Pulse Energy | >250 mJ
Repetition Rate | 10 Hz
Pulsewidth | >200 ns
Linewidth | Single frequency
Beam Quality | M2 < 1.2
Diode Current | 30% derating from maximum operating current
Cooling | Conduction cooled gain modules
Volume | <0.075 m3
Weight | <30 kg

## Slide 8: Design Features
Tm,Ho gain medium
  2 µm emission without nonlinear conversion
  Compatible with diode pumping with an absorption peak near 792 nm
  Optimum performance at low temperatures
    Observed 2X gain in energy at -26°C
MOPA configuration using 3 side-pumped gain modules
  Oscillator and 2 amplifiers
  5 sided pumping
3 m cavity using a multi-fold telescopic resonator
Acousto-optic Q-switch
Injection seeded with a commercially available single frequency source (Lockheed Martin Coherent Technologies Meteor)
  The cavity length is dithered via a PZT
  Electronics fire the Q-switch when a cavity resonance is detected

## Slide 9: Laser Concept
Laser bench
Installed inside
cylindrical housing
Coolant lines
or heat pipes
Seed path
(dashed)
Source not shown
Laser path
(solid) – 3 m
Round trip
Oscillator
Amplifiers
PZT
Isolators
Bench and housing designed for
maximum mechanical strength
and stability

## Slide 10: Laser Bench – Oscillator Configuration
Alignments performed
with lockable Risley prisms
Seed laser
fiber output
Isolator
Seed fold
mirror
Oscillator
PZT
Q-Switch
Bench Dimensions: 45.5” L x 6.45” W x 2.75” H
Volume = 0.13 m3

## Slide 11: Pump Module Design
Rod held
By 5 heat sinks
Diode light
Coupled into rod
Between heat sinks
Assembled Oscillator
Pump Module

## Slide 12: Optimum Performance to Date 1 Hz, 750 µs, 79 A, 5°C
1.9 µs build-up time
250 ns pulsewidth
Single Frequency
 | Pulse Energy (100 pulse avg.)
Long Pulse | 97 mJ
Q-Switched | 47.5 mJ
49% Q-switching Efficiency
37” from OC

## Slide 13: Additional Performance Notes
<3% RMS energy stability
~30% derating from peak current
5°C operating temperature
Single frequency determination made from clean profile recorded using a 500 MHz detector and 200 MHz oscilloscope
  Longitudinal mode spacing ~50 MHz

## Slide 14: SINGLE Frequency LASERS for space based wind & aerosol lidar

## Slide 15: Program Background
Phase 2 NASA SBIR
Two separate CW laser builds:
  Multiwavelength seed laser (1064, 532, 355 nm) frequency locked to an iodine cell (using the 532 nm output) to provide a multiwavelength single frequency source
    Delivering hardened brassboard laser with a frequency locking module
  2 µm seed laser
    Delivering proof of concept hardened breadboard
    No frequency control required for this program

## Slide 16: 2 Micron Seed Laser
Compact Tm,Ho ring laser
  Diode pumped
Designed for PZT cavity dithering, as applied on RRLT
Using ruggedized package concepts
Scheduled for completion in June 2011

## Slide 17: Summary
Fibertek is advancing the state of the art for multiple classes of 2 micron sources
First, hardened high pulse energy single frequency sources are under development to enable space-based wind measurements using coherent detection techniques
Second, CW lasers suitable for seeding the above high energy pulsed sources are under development
Will allow Fibertek to provide a complete single frequency 2 micron source compatible with airborne and space-based applications

## Slide 18: Support Equipment
FTS Low Temperature Chiller
(On Loan from NASA)
Meteor Seed Laser
Controller
Laser Head
Directed Energy Diode Drivers
Amplifier (1 of 2)
Oscillator
NEOS Q-Switch Driver
Control & Monitoring
Electronics

## Slide 19: Energy & Diode Wavelength vs. Temperature
Diodes sitting on
absorption peak
NOTE: The diode temperature measured is its mounting
plate and not the diode submount (isolation required).
Actual temperatures may be higher than these
measurements and the increased energies due to
walking the wavelength onto the peak.

## Slide 20: Next Steps
Quantify the alignment sensitivity of the current cavity configuration
Quantitatively measure the laser linewidth
Install thermistors on a selection of diodes to track their temperature
  Combine with OSA measurements to allow prediction of diode wavelength at any operating temperature
Install a dry box on the laser to allow operation at lower temperatures without the risk of condensation
Begin construction of the amplifier modules